TENDER: CFCU/0302.07-03//S/TR

"Supply of Equipment for Strengthening the Public Procurement System in Turkey"

CORRIGENDUM No. 1 to Tender Dossier

The following alterations and/ or corrections are made to the tender dossier. Please find below these alterations and/ or corrections.

Page 66: (TECHNICAL SPECIFICATIONS)

The former text:

# LOT-2: SATELLITE TERMINAL

2.1	HUB & REMOTE TERMINALS

2.1.1.	HUB TERMINAL

Detailed Technical Data (minimal technical specifications):

| Data rate | 256/1024 Mbps CIR 2048/8192 Mbps MIR The use of 512/512 rate for a period of 50 hours per a year should be guaranteed in the Contractor’s offer together with its use charge. Unused part of the 50 hour use will be transferred to the following year. |
| --- | --- |

Shall read as new text:

# LOT-2: SATELLITE TERMINAL

2.1	HUB & REMOTE TERMINALS

2.1.1.	HUB TERMINAL

Detailed Technical Data (minimal technical specifications):

| Data rate | 256/1024 Mbps CIR 2048/2048 Mbps MIR The use of 512/512 rate for a period of 50 hours per a year should be guaranteed in the Contractor’s offer together with its use charge. Unused part of the 50 hour use will be transferred to the following year. |
| --- | --- |

Page 67: (TECHNICAL SPECIFICATIONS)

The former text:

2.1.2.	REMOTE TERMINAL

2.1.2.1		UNIT INSIDE THE BUILDING (IDU)

Detailed Technical Data (minimal technical specifications):

| Data Transfer Rate | 16 Mbps download / 256 Kbps upload |
| --- | --- |

Shall read as new text:

2.1.2.	REMOTE TERMINAL

2.1.2.1		UNIT INSIDE THE BUILDING (IDU)

Detailed Technical Data (minimal technical specifications):

| Data Transfer Rate | 32 Kbps to 2048 Kbps download or upload |
| --- | --- |

Page 66: (TECHNICAL SPECIFICATIONS)

The former text:

# LOT-2: SATELLITE TERMINAL

2.1	HUB & REMOTE TERMINALS

2.1.1.	HUB TERMINAL

Detailed Technical Data (minimal technical specifications):

| Expansion features | TCP Accelerator, CIR, CAS, Firewall, Coding , QoS/Scalability, FAP |
| --- | --- |

Shall read as new text:

# LOT-2: SATELLITE TERMINAL

2.1	HUB & REMOTE TERMINALS

2.1.1.	HUB TERMINAL

Detailed Technical Data (minimal technical specifications):

| Expansion features | DELETED, CIR, CAS, Firewall, Coding , QoS/Scalability, FAP |
| --- | --- |

Page 67: (TECHNICAL SPECIFICATIONS)

The former text:

2.1.2.	REMOTE TERMINAL

2.1.2.1		UNIT INSIDE THE BUILDING (IDU)

Detailed Technical Data (minimal technical specifications):

| Accelerator | TCP accelerator |
| --- | --- |

Shall read as new text:

2.1.2.	REMOTE TERMINAL

2.1.2.1		UNIT INSIDE THE BUILDING (IDU)

Detailed Technical Data (minimal technical specifications):

| Accelerator | DELETED |
| --- | --- |

All other terms and conditions of the Tender dossier remain unchanged. The above alterations and / or corrections to the tender dossier are integral part of the Tender Dossier.

NOTE: All alterations and / or corrections to the tender dossier will be reflected to the Technical Evaluation Grid accordingly.