CHANGES NO.1 TO THE TENDER DOSSIER

| Contract Title: | Supply of Equipment for Renewable Energy for the Municipalities – Phase II |
| --- | --- |
| Publication Reference: | NEAR/ANK/2022/EA-OP/0017. |
| Location: | Türkiye |

The Tender Dossier is corrected or modified as follows:

ANNEX II + III TECHNICAL SPECIFICATIONS AND TECHNICAL OFFER

Technical Specifications

- Former Text:

| […] |
| --- |
| 1.4.8 | The system shall enable reporting extraordinary events, faults and errors occurred at SPP instantaneously to the e-mail address and GSM numbers specified by the beneficiary. |
| […] |

Shall read as:

| […] |
| --- |
| 1.4.8 | The system shall enable reporting extraordinary events, faults and errors occurred at SPP instantaneously to the e-mail addresses specified by the beneficiary. |
| […] |

- Former Text:

| […] |
| --- |
| 1.16.12 | Data acquired by the camera system shall be protected and stored safely to enable retrospective analysis for minimum up to 1 (one) year. System configuration and software shall not be affected from communication cuts. The system shall still be able to acquire and store data in case of a power and communication cuts for at least 24 (twenty-four) hours. Data stored during that period of time shall be transferrable to the server when reconnected. |
| […] |

Shall read as:

| […] |
| --- |
| 1.16.12 | Data acquired by the camera system shall be protected and stored safely to enable retrospective analysis for minimum up to 1 (one) month. System configuration and software shall not be affected from communication cuts. The system shall still be able to acquire and store data in case of a power and communication cuts for at least 24 (twenty-four) hours. Data stored during that period of time shall be transferrable to the server when reconnected. |
| […] |

- Former Text:

| […] |
| --- |
| 1.16.25 | MBS shall be equipped with multi sensor detectors such as fire, heat, smoke and CO2 detectors to identify dangerous situations. Divisions within the MBS shall be equipped separately with gas/water-combined extinguishing systems. |
| […] |

Shall read as:

| […] |
| --- |
| 1.16.25 | MBS shall be equipped with multi sensor detectors i.e. flame, heat, smoke and CO2 detectors to identify dangerous situations. Divisions within the MBS shall be equipped separately with gas/water-combined extinguishing systems. |
| […] |

- Former Text:

| […] |
| --- |
| 2.16.3 | Both MonoBlock Substation (Adiyaman Municipality Bahcecik SPP Transformer Station) and MonoBlock Substation (TIP2H-D) shall be equipped with multi sensor detectors such as fire, heat, smoke and CO2 detectors to identify dangerous situations. Divisions within each MBS shall be equipped separately with gas/water-combined extinguishing systems. |
| […] |

Shall read as:

| […] |
| --- |
| 2.16.3 | Both MonoBlock Substation (Adiyaman Municipality Bahcecik SPP Transformer Station) and MonoBlock Substation (TIP2H-D) shall be equipped with multi sensor detectors i.e. flame, heat, smoke and CO2 detectors to identify dangerous situations. Divisions within each MBS shall be equipped separately with gas/water-combined extinguishing systems. |
| […] |

- Former Text:

| […] |
| --- |
| 3.16.3 | Both MonoBlock Substation (Isparta Senirce SPP Transformer Station), Prefabricated Substation (Isparta Senirce SPP Distribution Station – PB3) and Connection Point Distribution Station shall be equipped with multi sensor detectors such as fire, heat, smoke and CO2 detectors to identify dangerous situations. Divisions within each Substation shall be equipped separately with gas/water-combined extinguishing systems. |
| […] |

Shall read as:

| […] |
| --- |
| 3.16.3 | Both MonoBlock Substation (Isparta Senirce SPP Transformer Station), Prefabricated Substation (Isparta Senirce SPP Distribution Station – PB3) and Connection Point Distribution Station shall be equipped with multi sensor detectors i.e. flame, heat, smoke and CO2 detectors to identify dangerous situations. Divisions within each Substation shall be equipped separately with gas/water-combined extinguishing systems. |
| […] |

All other terms and conditions of the tender dossier remain unchanged. The above alterations and /or corrections to the tender dossier are integral part of the tender dossier.