CHANGES No: 1

to the

TENDER DOSSIER

# Publication Ref: EuropeAid/139166/IH/SUP/TR

Subject: Supply of Equipment for Capacity Building for Effective Nationality Determination

Location: Turkey (TR)

The following alterations/changes are made to the Tender Dossier

## ANNEX II + III: TECHNICAL SPECIFICATIONS + TECHNICAL OFFER

## I - GENERAL REQUIREMENTS

C. General Technical Requirements

Shall read as new item:

[…]

xv. The customer has already a videoconference infrastructure. They have VC endpoints and communications manager. The Contractor will be responsible for the tasks required for the compatibility / interoperability of the new VC endpoint systems and MCU systems with the existing videoconference infrastructure.

II - TECHNICAL SPECIFICATIONS + TECHNICAL OFFER (ANNEX II + III)

LOT 2: VIDEO CONFERENCE EQUIPMENT

## Former Text:

[…]

| 2.1.1.2 | Support of at least 50 simultaneous participants in a VC session at HD resolution (720p/30fps) |
| --- | --- |

[…]

Shall read as:

[…]

| 2.1.1.2 | Support of at least 48 simultaneous participants in a VC session at HD resolution (720p/30fps) |
| --- | --- |

[…]

## Former Text:

[…]

| 2.1.6 | System for recording VC sessions and distribution of recorded content Type: Software based or appliance solutions are accepted |
| --- | --- |

[…]

Shall read as:

[…]

| 2.1.6 | System for recording VC sessions and distribution of recorded content Type: Software based or appliance solutions are accepted Duration: 1000 hours of recording with HD quality is required |
| --- | --- |

[…]

## Former Text:

[…]

| 2.1.8 | Client access licenses - quantity 600 The system should support access and participation to VC sessions from a personal computer or laptop (with appropriate microphone, speakers or headphones, and camera). The access should be allowed either by installing a dedicated software or by using a web browser. In case of a dedicated software it should run on MS Windows 7 or greater. The licenses for the access should be permanent with no limitation to participate in VC sessions (in duration, access to features like recording, etc.) |
| --- | --- |

[…]

Shall read as:

[…]

| 2.1.8 | The system should support access and participation to VC sessions from a personal computer or laptop (with appropriate microphone, speakers or headphones, and camera). The access should be allowed either by installing a dedicated software or by using a web browser. In case of a dedicated software it should run on MS Windows 7 or greater. The access shall be permanent with no limitation to participate in VC sessions (in duration, access to features like recording, etc.) In case it is required to have a license to satisfy this specification, at least 600 client access licenses shall be provided. In case it is not required to have a license to satisfy this specification, the proposed system shall allow participation of at least 600 VC clients. |
| --- | --- |

[…]

## Former Text:

[…]

| 2.2.3 | Video: - resolutions supported: 720p/60fps, 1080p/30fps or greater |
| --- | --- |

[…]

Shall read as:

[…]

| 2.2.3 | Video: - resolutions supported: 720p/60fps or 1080p/30fps or greater |
| --- | --- |

[…]

***

All other terms and conditions of the tender dossier remain unchanged. The above alterations and /or corrections to the tender dossier are integral part of the tender dossier.