CHANGES No.2 to TENDER DOSSIER

| Contract Title: | Construction of Community Centers for Support to Internally Displaced Persons in the Province of Van |
| --- | --- |
| Publication Reference: | EuropeAid/139926/ID/WKS/TR |

The following alterations and/or corrections are made to the Tender Dossier:

VOLUME 3 TECHNICAL SPECIFICATIONS 4 SPECIAL TECHNICAL SPECIFICATIONS 4.1 COMMUNITY CENTER AND GYMNASIUM CONSTRUCTION WORKS 4.1.1 CONSTRUCTION WORKS ARC_011 Pumice Add new text at the beginning of section: The pumice with volcanic origin, silicate based porous structure shall have aggregates with dimensional range of 10-30 mm and it shall be weighed 500kg/m3 including porosity. There will not be any particles of sand and/or cement in/around the pumice. ARC_016 Mechanically Installed Natural Stone Facade The former text: … SUMMARY Content: Complying with the technical specifications document, the application of the mechanically installed travertine natural stone facade must be in accordance with the design drawings and the standards listed below. … Shall read as new text: … SUMMARY Content: In line with the technical specifications document, the application of the mechanically installed natural stone (Denizli travertine or equivalent to be approved by the Engineer) facade must be in accordance with the design drawings and the relevant standards listed below. … ARC_016A Mechanical Stone Facade Covering with Special Workmanship The former text: … List of Operations for 1 m2 Mechanical Stone Façade including; Mechanical Stone Facade Special Workmanship Cost of Broadstone in Curved Surface of Travertine Specialist Broadstone Mason Specialist Broadstone Mason Helper 600 Dosage Cement And Colored Stone Brass Mortar Making … SUMMARY Content: Complying with the technical specifications document, the application of the mechanically installed travertine natural stone facade must be in accordance with the design drawings and the standards listed below. … Shall read as new text: … List of Operations for 1 m2 Mechanical Stone Façade including; Mechanical Stone Facade Special Workmanship Cost of Broadstone in Curved Surface of Travertine (Denizli travertine or equivalent to be approved by the Engineer) Specialist Broadstone Mason Specialist Broadstone Mason Helper 600 Dosage Cement And Colored Stone Brass Mortar Making … SUMMARY Content: In line with the technical specifications document, the application of the mechanical stone façade covering with special workmanship (Denizli travertine or equivalent to be approved by the Engineer) must be in accordance with the design drawings and the relevant standards listed below. … VOLUME 5 Drawing Sheets EDREMIT/IPEKYOLU/TUŞBA The former text in all drawing sheets: … ARC_034 6 CM (SANDWICH SYSTEM) ROCK WOOL … Shall read as new text: … ARC-34 ‘’Applying Thermal And Sound Insulation Between Two Walls Using 6 Cm-Thick Glass Wool Slabs (With A Density Of 20–22 Kg/M3 - Non-Load-Bearing, With Silicone) (Sandwich System) …

All other terms and conditions of the Tender Dossier remain unchanged. The above alterations and / or corrections to the tender dossier are an integral part of the Tender Dossier.

***