CHANGES NO:1 to

WORKS TENDER DOSSIER

| Contract Title: | Construction Works for Strengthening the Institutional Capacity of Gendarmerie General Command Regarding Public Order Management and Crowd Control |
| --- | --- |
| Publication Reference: | EuropeAid/138751/ID/WKS/TR |

Further to the requests received from the tenderers, the following changes have been made to Tender Dossier:

Under Volume 3 – Technical Specifications: Under Article General A 003, Add new bullets: Y: The costs related to training the personnel of the Beneficiary and costs related to any other services as per provisions of the Contract. Under Article 3.2 Heavy Current Installation, Add additional specification: Disassembly / Assembly Works: Regarding any disassembly / assembly works including but not limited to services mentioned under items ELC_126, ELC_127, ELC_128, ELC_129 and ELC_130; the Contractor is required to carry out related disassembly / assembly works in a short time up to 3 hours. In this regard, the Contractor will make all the services and equipment available and in place before demounting the existing cable, and finalise the assembly of the new line in up to 3 hours. Under Article ARC_043 Performing two layers of antirust and two layers of synthetic paint for iron surfaces, Add additional specification: Alkyd resin based highly synthetic rust inhibitor. Resistant to moisture and sulphate salts At least 77% solids Viscosity at least 90KU The specific gravity will be at least 1,5. Add new specification: MEC_124 112.00m3 Prismatic modular galvanized water storage Water storage will be made up from deep drawing sheets according to TSE standards and in DIN 1614 quality; and will be covered with hot galvanizing method. After all cutting, bending, drilling, welding and forming processes are finished, all parts of the water storage will be covered with “hot galvanize”. The coating should be in accordance with ISO 1461: 2009. After galvanizing, any welding process should be avoided. Supply of modular water storage made of steel coated with hot-dip galvanize, all interior and exterior materials, tensioning rods, bolts, feet, installation in the workplace by connecting to the foundation and plumbing are included. Note: Tank thicknesses will be at least 2,5 mm.

Under Volume 4.3.2 — Bill Of Quantities: Add new item: PRICE No TITLE UNIT UNIT PRICE ESTIMATED QUANTITIES AMOUNT MEC_124 112.00m3 Prismatic modular galvanized water storage PCS 1,00

Under Volume 4.3.3 — Price Schedules: Add new Price Schedule: PRICE No : MEC_124 Title: 112.00m3 Prismatic modular galvanized water storage All kind of materials for construction, workshop expenses, vertical and horizontal transportation in the workplace, unloading, workmanship, contractor’s general expenses and profit is included. This price is per PCS

All other terms and conditions of the tender dossier remain unchanged. The above alterations and /or corrections to the tender dossier are integral part of the tender dossier.