CHANGES NO:1 to

TENDER DOSSIER

| Contract Title: | Construction Works for Refurbishment and Maintenance of Removal Centres |
| --- | --- |
| Publication Reference: | EuropeAid/139903/ID/WKS/TR |

The following alterations and/or corrections are made to the Tender Dossier:

VOLUME 3 TECHNICAL SPECIFICATIONS 3.6.1.1. Interior Paint on Walls Add new text at the end of section: “(c) The damaged parts of plaster will be removed; the surfaces will be repaired in line with the provisions of Article 3.4.2. Plastering of Technical Specifications with plaster/mortar in order to achieve a smooth surface, the surfaces to be painted will be cleaned with wire brush, and the surfaces will be prepared for painting by applying 0,260 kg stain-concealing thermoplastic resin based primer.” 3.7. Doors Add new text under the heading: For doors, the blind casing will be carried out according to drawings; and related demolition, modification, blind casing costs will be included in the unit prices. 3.7.2. Internal Timber Doors Add new text at the end of bullet (c): The trim of the casing will be arranged to close the gap and space between the wall and the casing will be filled with polyurethane foam and it is included in the unit prices. 3.7.4. Entrance system with card reader The item is removed from the technical specifications and scope of works. 3.8. Windows Add new text under the heading: For windows, the blind casing will be carried out according to drawings; and related demolition, modification, blind casing costs will be included in the unit prices. 3.9. Roof The former text: “Waterproofing with polymer bitumen sheets with plastomer based polyester seal carrier at 3cm thickness under roof covering at sloped roofs will be conducted.” Shall read as new text: “Waterproofing with polymer bitumen sheets with plastomer based polyester seal carrier at 3mm thickness under roof covering at sloped roofs will be conducted.” 3.10. Dismantling Works Add new text at the end of section: For Adana and Van centers; the perimeter wall, fence and electric/camera poles will be removed. For Van center details related to existing facilities are as follows, There are around 50 electric poles to be removed and reinstalled, There is a concrete wall with average thickness of around 25 cm. The average height of walls is around 160 cm for the entrance walls and the two sides, average height of walls is around 250 cm for the back side. Length of the walls is around the same length with the proposed new wall that can be seen from the drawings. Above the concrete wall, there is a fence with around 180 cm height. For Adana center details related to existing facilities are as follows, There are around 6 camera poles to be removed and reinstalled, There is a concrete wall with average thickness of around 30 cm, average height of around 40 cm and length is around the same length with the proposed new wall that can be seen from the drawings. Above the concrete wall, there is a fence with around 200 cm height. Dismantling and demolition of the abovementioned materials, cleaning of their locations, transportation of rubble material to dump site to be arranged by the Contractor in consultation with local authorities, reinstallation of the electric/camera poles, all kinds of materials, workmanship, tools and equipment expenses, contractor general expenses and profit will be included in the tender prices. The beneficiary will have the rights of the materials removed or demolished. For each dismantling or demolishing works, the Engineer in consultation with the beneficiary shall decide and inform the contractor. In case the beneficiary intends to keep the removed or demolished materials, the materials to be kept shall be handed over to the beneficiary personnel for receipt and stored in the location as directed. The remaining parts shall be moved out of the site by the contractor to a deposit site arranged by the contractor in consultation with local authorities. 4.2.3.2. SOLAR COLLECTORS WITH SELECTIVE SURFACE The item is removed from the technical specifications and scope of works. 4.2.5. 10,00 m3 Stainless steel water tank The item is removed from the technical specifications and scope of works. 4.2.6. Package type cold storage device The item is removed from the technical specifications and scope of works. 4.2.7. PVC coated cold air storage doors The item is removed from the technical specifications and scope of works. 4.2.8. Modular type wall, ceiling and floor panels The item is removed from the technical specifications and scope of works. 4.3. COOLING INSTALLMENT Add new text under the heading: Cabling and drain line for units in cooling system will be installed with plastic protection channels and the energy will be supplied from electric panels. The plastic protection channels will be placed on the plaster. All the cabling and drain line works indicated above shall be included in the unit prices of the units. 4.3.4. Wall Type Indoor Unit Add new text at the end of section: “Drain pipe will be plastic 20 mm pipe running from A.C. units outside up to 10m away from the location of the A.C. unit (to the yard, green areas, rain pipes). All the works indicated above shall be included in the unit prices.” 4.4. HEATING SYSTEM The former text: “The heating boilers made of steel available on site will be disassembled to install new boilers. New boilers will be supplied and installed with capacity (90.000 kcal/h) 100 kw. They will conform to TS EN 12952-1, TS EN 12952-3, TS EN 303–5 standards with min. 3 atmospheric construction pressure capacity. Materials including losses, transportation to site together with all relevant materials, engineering studies, installation and mounting, piping, electrical, automatic control and accessory making, commissioning, testing, workmanship, contractor’s profit and general expenses for functional delivery of the item are included.” Shall read as new text: “A solid fuel (coal) boiler will be installed with capacity (540.000 kcal/h) 630 kw conforming with TS EN 12953-1 and TS EN 12953-3 standards. The boiler will have min. 3 atmospheric construction pressure capacity. Thermodynamic and strength calculations will be presented according to the indicated construction pressure. Capacity and efficiency test reports will be performed and presented according to the above mentioned standards. Capacity and thermal efficiency values obtained as a result of the capacity and thermal efficiency tests will not be lower than the values in TSE (Turkish Standards institute). The boiler will be installed with all accessories and stokers on a concrete base and delivered in working condition. Note: The boilers shall be in accordance with the applicable provisions of the Pressure Equipment Directive 97/23 / EC (Annex-1) Article 2.10, Article 2.11, Article 3.4, Article 5 (a) and Article 5 (ç) and; the basic requirements mentioned under directives “Control of Air Pollution Caused by Heating” and “Control of Air Pollution Caused by Industry”. Materials including losses, transportation to site together with all relevant materials, engineering studies, installation and mounting, piping, electrical, automatic control and accessory making, commissioning, testing, workmanship, contractor’s profit and general expenses for functional delivery of the item is included in this unit price.” 5.1.1. Fire Detection Technical Specifications Add new text under the heading: Disassembling of the existing items for Fire Detection Systems will be carried out by the Contractor and they are included in the unit prices. The beneficiary will have the rights of the materials removed or demolished. For each dismantling or demolishing works, the Engineer in consultation with the beneficiary shall decide and inform the contractor. In case the beneficiary intends to keep the removed or demolished materials, the materials to be kept shall be handed over to the beneficiary personnel for receipt and stored in the location as directed. The remaining parts shall be moved out of the site by the contractor to a deposit site arranged by the contractor in consultation with local authorities. 5.1.2. CCTV SYSTEM TECHNICAL SPECIFICATIONS Add new text under the heading: Disassembling of the existing items for CCTV Systems will be carried out by the Contractor and they are included in the unit prices. The beneficiary will have the rights of the materials removed or demolished. For each dismantling or demolishing works, the Engineer in consultation with the beneficiary shall decide and inform the contractor. In case the beneficiary intends to keep the removed or demolished materials, the materials to be kept shall be handed over to the beneficiary personnel for receipt and stored in the location as directed. The remaining parts shall be moved out of the site by the contractor to a deposit site arranged by the contractor in consultation with local authorities. 5.1.3.1. 150 KVA Standby / 150 KVA Prime Fully Automatic Diesel Electrogen Group Technical Specifications 08- Daily and Main Fuel Tanks: The former text: “The engine shall be fed from a daily fuel reservoir that has a capacity sufficient for running for at least 11 hours at 100% load.” Shall read as new text: “New fuel tank will be provided for the generator and it is included in the unit price. Fuel Tank shall be double walled, manufactured from ST 37-2 carbon steel and according to TSE EN 12285-1 and 2. The tanks will also be insulated taking into account weather conditions of the locations to be installed. The fuel reservoir shall have a capacity sufficient for running for at least 11 hours at 100% load. The generator will be delivered with full tank and fuel costs will also be included in the unit price.” Add new heading and text as follows: 12- Cabin The generator will be placed outside and a cabin will be installed. The cabin cover shall be at least 1.8 mm thick galvanised sheets with dimensions conforming with the generator proposed by the Contractor. The cabin shall be waterproof. The walls shall be electrostatic powder painted. The cabin shall have lockable doors. The cabin shall also be insulated with inflammable material. The cabin shall also be placed on a reinforced concrete block at least 30 cm above the ground level. All the works included above shall be included in the unit price of the generator. 5.1.3.2. 300 KVA Standby / 300 KVA Prime Fully Automatic Diesel Electrogen Group 08- Daily and Main Fuel Tanks: The former text: “The engine shall be fed from a daily fuel reservoir that has a capacity sufficient for running for at least 11 hours at 100% load.” Shall read as new text: “New fuel tank will be provided for the generator and it is included in the unit price. Fuel Tank shall be double walled, manufactured from ST 37-2 carbon steel and according to TSE EN 12285-1 and 2. The tanks will also be insulated taking into account weather conditions of the locations to be installed. The fuel reservoir shall to have a capacity sufficient for running for at least 11 hours at 100% load. The generator will be delivered with full tank and fuel costs will also be included in the unit price.” Add new heading and text as follows: 12- Cabin The generator will be placed outside and a cabin will be installed. The cabin cover shall be at least 1.8 mm thick galvanised sheets with dimensions conforming with the generator proposed by the Contractor. The cabin shall be waterproof. The walls shall be electrostatic powder painted. The cabin shall have lockable doors. The cabin shall also be insulated with inflammable material. The cabin shall also be placed on a reinforced concrete block at least 30 cm above the ground level. All the works included above shall be included in the unit price of the generator.

VOLUME 4.3.2 — BILL OF QUANTITIES The former text: PRICE No TITLE UNIT UNIT PRICE (EUR) ESTIMATED QUANTITIES AMOUNT (EUR) ADANA AYDIN EDIRNE HATAY VAN TOTAL (a) (b) (c) (d) (e) (f = d * e) … CW-TR-RC-021 Plastering with grain and fine mortar, 200/250 kg lime/cement mixture m² 36,00 105,00 148,00 28,00 115,00 432,00 … CW-TR-RC-028 Getting the stained and smudgy wall surfaces ready for painting m² 1.246,00 6.430,00 9.870,00 980,00 0,00 18.526,00 CW-TR-RC-029 Applying primer and two layers water based matte paint on old-painted surfaces (interior walls) m² 886,00 4.650,00 5.127,00 1.680,00 0,00 12.343,00 CW-TR-RC-030 Applying primer and two layers water based matte antibacterial paint on old-painted surfaces (interior walls) m² 945,00 3.785,00 4.040,00 1.450,00 0,00 10.220,00 … CW-TR-RC-046 Supply and Install 100 mm diameter zinc plate no. 12 Vertical rainpipe m 0,00 160,00 0,00 0,00 178,00 338,00 CW-TR-RC-047 Dismantling of all kinds of roof materials m² 0,00 2.247,00 0,00 0,00 3.220,00 5.467,00 CW-TR-RC-048 Tile transferring at all kinds of tile covered roofs m² 0,00 960,00 0,00 0,00 1.020,00 1.980,00 CW-TR-RC-049 Making roof covering with channel tile and top tile (impermeability class : Group 1) ( resistant to 150 freezing- thaw cycle) (3 lath system) m² 0,00 1.287,00 0,00 0,00 2.200,00 3.487,00 CW-TR-RC-050 Construction of wooden free standing roof (wooden roof sheathing) m² 0,00 2.247,00 0,00 0,00 3.220,00 5.467,00 CW-TR-RC-051 Conducting waterproofing with polymer bitumen sheets with plastomer based polyester seal carrier at 3cm thickness under roof covering at sloped roofs m² 0,00 2.247,00 0,00 0,00 3.220,00 5.467,00 … CW-TR-RC-053 Making horizontal valley gutter as waterspout from zinc plates no.14 m 0,00 455,00 0,00 0,00 628,00 1.083,00 … CW-TR-RC-056 Floor tiling with rectified, 1st quality, shiny, unglazed porcelain floor tiles at (30 x 30cm) or (33 x 33 cm) dimensions at any colour, design and surface features, at 3mm joint gaps (with tile adhesive) m² 0,00 2.120,00 380,00 0,00 940,00 3.440,00 … CW-TR-RC-059 Wall and facade tiling with rectified, 1st quality, shiny, unglazed porcelain floor tiles at (30 x 30cm) or (33 x 33 cm) dimensions at any colour, design and surface features, at 3mm joint gaps (with tile adhesive) m² 0,00 0,00 280,00 0,00 0,00 280,00 … MW- RC-HES-01-016 Heating boiler made of steel - (90.000 kcal/h) 100 kw pcs 0,00 0,00 0,00 0,00 2,00 2,00 …. Shall read as new text: PRICE No TITLE UNIT UNIT PRICE (EUR) ESTIMATED QUANTITIES AMOUNT (EUR) ADANA AYDIN EDIRNE HATAY VAN TOTAL (a) (b) (c) (d) (e) (f = d * e) … CW-TR-RC-021 Plastering with grain and fine mortar, 200/250 kg lime/cement mixture m² 310,00 855,00 1.045,00 345,00 920,00 3.475,00 … CW-TR-RC-028 Getting the stained and smudgy wall surfaces ready for painting m² 1.246,00 6.430,00 9.870,00 980,00 9.850,00 28.376,00 CW-TR-RC-029 Applying primer and two layers water based matte paint on old-painted surfaces (interior walls) m² 886,00 4.650,00 5.127,00 1.680,00 5.150,00 17.493,00 CW-TR-RC-030 Applying primer and two layers water based matte antibacterial paint on old-painted surfaces (interior walls) m² 945,00 3.785,00 4.040,00 1.450,00 4.050,00 14.270,00 … CW-TR-RC-046 Supply and Install 100 mm diameter zinc plate no. 12 Vertical rainpipe m 0,00 160,00 0,00 0,00 0,00 160,00 CW-TR-RC-047 Dismantling of all kinds of roof materials m² 0,00 2.247,00 0,00 0,00 0,00 2.247,00 CW-TR-RC-048 Tile transferring at all kinds of tile covered roofs m² 0,00 960,00 0,00 0,00 0,00 960,00 CW-TR-RC-049 Making roof covering with channel tile and top tile (impermeability class : Group 1) ( resistant to 150 freezing- thaw cycle) (3 lath system) m² 0,00 1.287,00 0,00 0,00 0,00 1.287,00 CW-TR-RC-050 Construction of wooden free standing roof (wooden roof sheathing) m² 0,00 2.247,00 0,00 0,00 0,00 2.247,00 CW-TR-RC-051 Conducting waterproofing with polymer bitumen sheets with plastomer based polyester seal carrier at 3mm thickness under roof covering at sloped roofs m² 0,00 2.247,00 0,00 0,00 0,00 2.247,00 … CW-TR-RC-053 Making horizontal valley gutter as waterspout from zinc plates no.14 m 0,00 455,00 0,00 0,00 0,00 455,00 … CW-TR-RC-056 Floor tiling with rectified/non-rectified, 1st quality, shiny, unglazed porcelain floor tiles at (30 x 30cm) or (33 x 33 cm) dimensions at any colour, design and surface features, at 3mm joint gaps (with tile adhesive) m² 150,00 2.120,00 380,00 250,00 940,00 3.840,00 … CW-TR-RC-059 Wall and facade tiling with rectified/non-rectified, 1st quality, shiny, unglazed porcelain floor tiles at (30 x 30cm) or (33 x 33 cm) dimensions at any colour, design and surface features, at 3mm joint gaps (with tile adhesive) m² 150,00 295,00 280,00 290,00 305,00 1.320,00 … MW- RC-HES-01-016 Heating boiler made of steel - (540.000 kcal/h) 630 kw pcs 0,00 0,00 0,00 0,00 2,00 2,00 … The following items are removed from the Bill of Quantities and scope of works. PRICE No TITLE UNIT UNIT PRICE (EUR) ESTIMATED QUANTITIES AMOUNT (EUR) ADANA AYDIN EDIRNE HATAY VAN TOTAL (a) (b) (c) (d) (e) (f = d * e) … CW-TR-RC-025 Entrance system with card reader pcs 6,00 0,00 0,00 0,00 0,00 6,00 … MW-RC-SAS-01-001 Solar Collector with selective surface m² 20,00 0,00 0,00 0,00 0,00 20,00 … MW-RC-SAS-01-005 10,00 m3 stainless steel water tank - prismatic modules pcs 0,00 0,00 0,00 0,00 1,00 1,00 MW-RC-SAS-01-006 Package type cold storage device (2000 kcal/h) freon 404 , hermetic compressor -15 / -25 °c pcs 0,00 0,00 0,00 0,00 1,00 1,00 MW-RC-SAS-01-007 PVC coated cold air storage doors with 12cm thick and 90 x 190 cm clear pass pcs 0,00 0,00 0,00 0,00 1,00 1,00 MW-RC-SAS-01-008 Modular type wall panel - both side are PVC coated or polyester painted and 12 cm thick m² 0,00 0,00 0,00 0,00 1,00 1,00 MW-RC-SAS-01-009 Modular type ceiling panel - both side are PVC coated or polyester painted and 12 cm thick m² 0,00 0,00 0,00 0,00 1,00 1,00 MW-RC-SAS-01-010 Modular type floor panel - Plywood coated and 12 cm thick m² 0,00 0,00 0,00 0,00 1,00 1,00 …

VOLUME 4.3.3 — PRICE SCHEDULE CW-TR-RC-024 The former text: PRICE No : CW-TR-RC-024 Title : Manufacturing and replacing solid wood panelled interior door trim and casing Price per m² including all kinds of required materials and losses, tools and devices, (excluding paint or polish) for manufacturing solid casing minimum at 45mm thickness from 1st class from white pine (fir tree) and double-sided trim minimum at 22mm thickness on interior doors in accordance with its drawings, fixing on each three wedges, when necessary, placing lathes on trim or casing side. All kind of materials for construction, workshop expenses, vertical and horizontal transportation in the workplace, unloading, workmanship, contractor’s general expenses and profit is included. This price is per m² Shall read as new text: PRICE No : CW-TR-RC-024 Title : Manufacturing and replacing solid wood panelled interior door trim and casing Price per m² including all kinds of required materials and losses, tools and devices, (excluding paint or polish) for manufacturing solid casing minimum at 45mm thickness from 1st class from white pine (fir tree) and double-sided trim minimum at 22mm thickness on interior doors in accordance with its drawings, fixing on each three wedges, when necessary, placing lathes on trim or casing side. The trim of the casing will be arranged to close the gaps and space between the wall and the casing will be filled with polyurethane foam and it is included in the unit prices All kind of materials for construction, workshop expenses, vertical and horizontal transportation in the workplace, unloading, workmanship, contractor’s general expenses and profit is included. This price is per m² CW-TR-RC-028 The former text: PRICE No : CW-TR-RC-028 Title : Getting the stained and smudgy wall surfaces ready for painting Price per m² for cleaning the to-be-paint surfaces with wire brush, preparing the surfaces for painting by applying 0,260 kg stain-concealing thermoplastic resin based primer. All kind of materials for construction, workshop expenses, vertical and horizontal transportation in the workplace, unloading, workmanship, contractor’s general expenses and profit is included. This price is per m² Shall read as new text: PRICE No : CW-TR-RC-028 Title : Getting the stained and smudgy wall surfaces ready for painting Price per m² for removal of damaged plaster, repairing the surfaces with plaster/mortar in order to achieve a smooth surface, cleaning the surfaces to be painted with wire brush, and preparing the surfaces for painting by applying 0,260 kg stain-concealing thermoplastic resin based primer. All kind of materials for construction, workshop expenses, vertical and horizontal transportation in the workplace, unloading, workmanship, contractor’s general expenses and profit is included. This price is per m² CW-TR-RC-051 The former text: PRICE No : CW-TR-RC-051 Title : Conducting waterproofing with polymer bitumen sheets with plastomer based polyester seal carrier at 3cm thickness under roof covering at sloped roofs Price per m² including expenses for all kinds of material and losses, workmanship, loading at worksite, vertical and horizontal handling, unloading, contractor’s general expenses and profit for cleaning the sloped roof surface, laying polymer bitumen sheets with plastomer based polyester seal carrier at 3cm thickness as parallel to eaves line and as overlapping to each other at least 10cm, fixing with galvanised large-headed spikes at least at 10cm intervals under junction pieces and gluing the junctions with torch fire in compliance with drawings. This price is per m² Shall read as new text: PRICE No : CW-TR-RC-051 Title : Conducting waterproofing with polymer bitumen sheets with plastomer based polyester seal carrier at 3mm thickness under roof covering at sloped roofs Price per m² including expenses for all kinds of material and losses, workmanship, loading at worksite, vertical and horizontal handling, unloading, contractor’s general expenses and profit for cleaning the sloped roof surface, laying polymer bitumen sheets with plastomer based polyester seal carrier at 3mm thickness as parallel to eaves line and as overlapping to each other at least 10cm, fixing with galvanised large-headed spikes at least at 10cm intervals under junction pieces and gluing the junctions with torch fire in compliance with drawings. This price is per m² CW-TR-RC-056 The former text: PRICE No : CW-TR-RC-056 Title : Floor tiling with rectified, 1st quality, shiny, unglazed porcelain floor tiles at (30 x 30cm) or (33 x 33 cm) dimensions at any colour, design and surface features, at 3mm joint gaps (with tile adhesive) Price per m² including expenses for all kinds of material and losses, workmanship, tools and devices, loading at worksite, vertical and horizontal handling, unloading, contractor’s general expenses and profit for purifying the smooth surface from dirt, dust, burs and such remains, preventer to adhesion, and moisturising, applying on surface cement based high performance tile adhesive of which slipping feature is diminished and period of open waiting is increased, and fluting with special dredge, laying rectified, 1st quality, shiny, unglazed porcelain floor tiles at (30 x 30cm) or (33 x 33 cm) dimensions at any colour, design and surface features, at 3mm joint gaps, filling the joints with cement based, high performance, resistant to high corrosion joint filler at any colour, of which water sorption is decreased, cleaning the covered area in compliance with approved detail project. This price is per m² Shall read as new text: PRICE No : CW-TR-RC-056 Title : Floor tiling with rectified/non-rectified, 1st quality, shiny, unglazed porcelain floor tiles at (30 x 30cm) or (33 x 33 cm) dimensions at any colour, design and surface features, at 3mm joint gaps (with tile adhesive) Price per m² including expenses for all kinds of material and losses, workmanship, tools and devices, loading at worksite, vertical and horizontal handling, unloading, contractor’s general expenses and profit for purifying the smooth surface from dirt, dust, burs and such remains, preventer to adhesion, and moisturising, applying on surface cement based high performance tile adhesive of which slipping feature is diminished and period of open waiting is increased, and fluting with special dredge, laying rectified/non-rectified, 1st quality, shiny, unglazed porcelain floor tiles at (30 x 30cm) or (33 x 33 cm) dimensions at any colour, design and surface features, at 3mm joint gaps, filling the joints with cement based, high performance, resistant to high corrosion joint filler at any colour, of which water sorption is decreased, cleaning the covered area in compliance with approved detail project. This price is per m² CW-TR-RC-059 The former text: PRICE No : CW-TR-RC-059 Title : Wall and facade tiling with rectified, 1st quality, shiny, unglazed porcelain floor tiles at (30 x 30cm) or (33 x 33 cm) dimensions at any colour, design and surface features, at 3mm joint gaps (with tile adhesive) Price per m² including expenses for all kinds of material and losses, workmanship, tools and devices, loading at worksite, vertical and horizontal handling, unloading, contractor’s general expenses and profit for purifying the smooth surface from remaining materials preventing the adhesion such as dirt, dust, burs and alike, and moisturising, applying on surface cement based high performance tile adhesive of which slipping feature is diminished and period of open waiting is increased, and fluting with special dredge, laying rectified, 1st quality, shiny, unglazed porcelain floor tiles at (30 x 30cm) or (33 x 33 cm) dimensions at any colour, design and surface features, at 3mm joint gaps, filling the joints with cement based, high performance, resistant to high corrosion joint filler at any colour, of which water sorption is decreased, cleaning the covered area in compliance with drawings. This price is per m² Shall read as new text: PRICE No : CW-TR-RC-059 Title : Wall and facade tiling with rectified/non-rectified, 1st quality, shiny, unglazed porcelain floor tiles at (30 x 30cm) or (33 x 33 cm) dimensions at any colour, design and surface features, at 3mm joint gaps (with tile adhesive) Price per m² including expenses for all kinds of material and losses, workmanship, tools and devices, loading at worksite, vertical and horizontal handling, unloading, contractor’s general expenses and profit for purifying the smooth surface from remaining materials preventing the adhesion such as dirt, dust, burs and alike, and moisturising, applying on surface cement based high performance tile adhesive of which slipping feature is diminished and period of open waiting is increased, and fluting with special dredge, laying rectified/non-rectified, 1st quality, shiny, unglazed porcelain floor tiles at (30 x 30cm) or (33 x 33 cm) dimensions at any colour, design and surface features, at 3mm joint gaps, filling the joints with cement based, high performance, resistant to high corrosion joint filler at any colour, of which water sorption is decreased, cleaning the covered area in compliance with drawings. This price is per m² MW-RC-HES-01-016 The former text: PRICE No : MW-RC-HES-01-016 Title : Heating boiler made of steel - (90.000 kcal/h) 100 kw A boiler will be supplied and installed. Capacity will be (90.000 kcal/h) 100 kw. It will have TS EN 12952-1, TS EN 12952-3, TS EN 303–5 standards. With min. 3 atmospheric construction pressure capacity. Materials including losses, transportation to site together with all relevant materials, engineering studies, installation and mounting, piping, electrical, automatic control and accessory making, commissioning, testing, workmanship, contractor’s profit and general expenses for functional delivery of the item is included in this unit price. This price is per pcs Shall read as new text: PRICE No : MW-RC-HES-01-016 Title : Heating boiler made of steel - (540.000 kcal/h) 630 kw A solid fuel (coal) boiler will be installed with capacity (540.000 kcal/h) 630 kw conforming with TS EN 12953-1 and TS EN 12953-3 standards. The boiler will have min. 3 atmospheric construction pressure capacity. Thermodynamic and strength calculations will be presented according to the indicated construction pressure. Capacity and efficiency test reports will be performed and presented according to the above mentioned standards. Capacity and thermal efficiency values ​​obtained as a result of the capacity and thermal efficiency tests will not be lower than the values in TSE (Turkish Standards institute). The boiler will be installed with all accessories and stokers on a concrete base and delivered in working condition. Note: The boilers shall be in accordance with the applicable provisions of the Pressure Equipment Directive 97/23 / EC (Annex-1) Article 2.10, Article 2.11, Article 3.4, Article 5 (a) and Article 5 (ç) and; the basic requirements mentioned under directives “Control of Air Pollution Caused by Heating” and “Control of Air Pollution Caused by Industry”. Materials including losses, transportation to site together with all relevant materials, engineering studies, installation and mounting, piping, electrical, automatic control and accessory making, commissioning, testing, workmanship, contractor’s profit and general expenses for functional delivery of the item is included in this unit price. This price is per pcs MW-RC-VES-01-006 The former text: PRICE No : MW-RC-VES-01-006 Title : Wall Type Indoor Unit with 3,6 kW cooling capacity (nom) The 3,6KW unit will be operable with cooling gases. It will have all the necessary CE standards. Microprocessor control unit will be installed. All the efficiency calculations will be documented. All materials including losses, transportation to site together with all relevant materials, engineering studies, installation and mounting, piping, electrical, automatic control and accessory making, commissioning, testing, workmanship, contractor’s profit and general expenses for functional delivery of the item is included in this unit price. This price is per pcs Shall read as new text: PRICE No : MW-RC-VES-01-006 Title : Wall Type Indoor Unit with 3,6 kW cooling capacity (nom) The 3,6KW unit will be operable with cooling gases. It will have all the necessary CE standards. Microprocessor control unit will be installed. All the efficiency calculations will be documented. All materials including losses, transportation to site together with all relevant materials, engineering studies, installation and mounting, piping, electrical cabling and drain lines, automatic control and accessory making, commissioning, testing, workmanship, contractor’s profit and general expenses for functional delivery of the item is included in this unit price. This price is per pcs MW-RC-VES-01-009 The former text: PRICE No : MW-RC-VES-01-009 Title : Central control unit up to 50 internal units Central control unit up to 50 internal units shall be installed as per the requirements in technical specifications. All kind of materials for construction, workshop expenses, vertical and horizontal transportation in the workplace, unloading, workmanship, contractor’s general expenses and profit is included. This price is per pcs Shall read as new text: PRICE No : MW-RC-VES-01-009 Title : Central control unit up to 50 internal units Central control unit up to 50 internal units shall be installed as per the requirements in technical specifications. All kind of materials for construction, electrical cabling and drain lines, workshop expenses, vertical and horizontal transportation in the workplace, unloading, workmanship, contractor’s general expenses and profit is included. This price is per pcs MW-RC-VES-01-020 The former text: PRICE No : MW-RC-VES-01-020 Title : Outdoor Unit with 28,8 kW cooling capacity (nom) The 28,8 KW unit will be operable with cooling gases. It will have all the necessary CE standards. Microprocessor control unit will be installed. All the efficiency calculations will be documented. All materials including losses, transportation to site together with all relevant materials, engineering studies, installation and mounting, piping, electrical, automatic control and accessory making, commissioning, testing, workmanship, contractor’s profit and general expenses for functional delivery of the item is included in this unit price. This price is per pcs Shall read as new text: PRICE No : MW-RC-VES-01-020 Title : Outdoor Unit with 28,8 kW cooling capacity (nom) The 28,8 KW unit will be operable with cooling gases. It will have all the necessary CE standards. Microprocessor control unit will be installed. All the efficiency calculations will be documented. All materials including losses, transportation to site together with all relevant materials, engineering studies, installation and mounting, piping, electrical cabling and drain lines, automatic control and accessory making, commissioning, testing, workmanship, contractor’s profit and general expenses for functional delivery of the item is included in this unit price. This price is per pcs MW-RC-VES-01-21 The former text: PRICE No : MW-RC-VES-01-21 Title : Outdoor Unit with 72 kW cooling capacity (nom) The 72 KW unit will be operable with cooling gases. It will have all the necessary CE standards. Microprocessor control unit will be installed. All the efficiency calculations will be documented. All materials including losses, transportation to site together with all relevant materials, engineering studies, installation and mounting, piping, electrical, automatic control and accessory making, commissioning, testing, workmanship, contractor’s profit and general expenses for functional delivery of the item is included in this unit price. This price is per pcs Shall read as new text: PRICE No : MW-RC-VES-01-21 Title : Outdoor Unit with 72 kW cooling capacity (nom) The 72 KW unit will be operable with cooling gases. It will have all the necessary CE standards. Microprocessor control unit will be installed. All the efficiency calculations will be documented. All materials including losses, transportation to site together with all relevant materials, engineering studies, installation and mounting, piping, electrical cabling and drain lines, automatic control and accessory making, commissioning, testing, workmanship, contractor’s profit and general expenses for functional delivery of the item is included in this unit price. This price is per pcs MW-RC-VES-01-022 The former text: PRICE No : MW-RC-VES-01-022 Title : Outdoor Unit with 79,2 kW cooling capacity (nom) The 79,2 KW unit will be operable with cooling gases. It will have all the necessary CE standards. Microprocessor control unit will be installed. All the efficiency calculations will be documented. All materials including losses, transportation to site together with all relevant materials, engineering studies, installation and mounting, piping, electrical, automatic control and accessory making, commissioning, testing, workmanship, contractor’s profit and general expenses for functional delivery of the item is included in this unit price. This price is per pcs Shall read as new text: PRICE No : MW-RC-VES-01-022 Title : Outdoor Unit with 79,2 kW cooling capacity (nom) The 79,2 KW unit will be operable with cooling gases. It will have all the necessary CE standards. Microprocessor control unit will be installed. All the efficiency calculations will be documented. All materials including losses, transportation to site together with all relevant materials, engineering studies, installation and mounting, piping, electrical cabling and drain lines, automatic control and accessory making, commissioning, testing, workmanship, contractor’s profit and general expenses for functional delivery of the item is included in this unit price. This price is per pcs EW-RC-GNR-01-004 The former text: PRICE No : EW-RC-GNR-01-004 Title : Diesel generator set supplies 1500 rpm 150 kva Supplying and installing Diesel generator set supplies 1500 rpm 150 kva as per the requirements in technical specifications. These technical specifications describe the Electrogen Group with 1 piece of 150 kVA standby / 150 kVA prime Diesel-Cabin and ATS Panel, which automatically go and charge itself with totally 150 kVA stand-by load in 0-7 seconds, when the city network power that supplies the building is disrupted, a phase is lost or the voltage or frequency goes out of the normal limits. 1 piece of Diesel-Electrogen Group with 150 kVA PRIME / 150 kVA STANDBY output power will be installed. This group being designed according to the applicable standards of ANSI, NEC, ISO, UL, IEEE and NEMA, its power will be determined, and being tested, will be packaged. The diesel generator set shall be manufactured by a manufacturer with ISO 9001 quality assurance certificate. Electrogen group; consists of the diesel engine, the alternator directly driven by the engine as well as type force, control, protection panels which are mounted in separate place. The Diesel - Generator set shall be combined by directly coupling on a common chassis. All parts and materials used in the generator group shall be unused. Generator Set Specifications Prime Net Power : 120 ekW / 150 kVA Standby Net Power : 120 ekW / 150 kVA Alternator Output Voltage: 400 Volts / 3 phases Frequency / Rotation : 50 Hz / 1500 rpm. Power Factor : 0.8 Voltage Regulation : + - 0.5% Waveform NEMA : 50 Wave Form IEC :% 2 Total Harmonic Content: 4% (LL /LN) All necessary materials including losses, transportation to site together with all relevant materials, installation and mounting, commissioning, testing, workmanship, contractor’s profit and general expenses for functional delivery of the item is included in this unit price. This price is per pcs Shall read as new text: PRICE No : EW-RC-GNR-01-004 Title : Diesel generator set supplies 1500 rpm 150 kva Supplying and installing Diesel generator set supplies 1500 rpm 150 kva as per the requirements in technical specifications. These technical specifications describe the Electrogen Group with 1 piece of 150 kVA standby / 150 kVA prime Diesel-Cabin and ATS Panel, which automatically go and charge itself with totally 150 kVA stand-by load in 0-7 seconds, when the city network power that supplies the building is disrupted, a phase is lost or the voltage or frequency goes out of the normal limits. 1 piece of Diesel-Electrogen Group with 150 kVA PRIME / 150 kVA STANDBY output power will be installed. This group being designed according to the applicable standards of ANSI, NEC, ISO, UL, IEEE and NEMA, its power will be determined, and being tested, will be packaged. The diesel generator set shall be manufactured by a manufacturer with ISO 9001 quality assurance certificate. Electrogen group; consists of the diesel engine, the alternator directly driven by the engine as well as type force, control, protection panels which are mounted in separate place. The Diesel - Generator set shall be combined by directly coupling on a common chassis. All parts and materials used in the generator group shall be unused. Generator Set Specifications Prime Net Power : 120 ekW / 150 kVA Standby Net Power : 120 ekW / 150 kVA Alternator Output Voltage: 400 Volts / 3 phases Frequency / Rotation : 50 Hz / 1500 rpm. Power Factor : 0.8 Voltage Regulation : + - 0.5% Waveform NEMA : 50 Wave Form IEC :% 2 Total Harmonic Content: 4% (LL /LN) New fuel tank will be provided for the generator and it is included in the unit price. Fuel Tank shall be double walled, manufactured from ST 37-2 carbon steel and according to TSE EN 12285-1 and 2. The tanks will also be insulated taking into account weather conditions of the locations to be installed. The fuel reservoir need to have a capacity sufficient for running for at least 11 hours at 100% load. The generator will be delivered with full tank and fuel costs will also be included in the unit price. The generator will be placed outside and a cabin will be installed. The cabin cover shall be at least 1.8 mm thick galvanised sheets with dimensions conforming with the generator proposed by the Contractor. The cabin shall be waterproof. The walls shall be electrostatic powder painted. The cabin shall have lockable doors. The cabin shall also be insulated with inflammable material. The cabin shall also be placed on a reinforced concrete block at least 30 cm above the ground level. All the works included above shall be included in the unit price of the generator. All necessary materials including losses, transportation to site together with all relevant materials, installation and mounting, commissioning, testing, workmanship, contractor’s profit and general expenses for functional delivery of the item is included in this unit price. This price is per pcs MW-RC-VES-01-022 The former text: PRICE No : EW-RC-GNR-01-018 Title : Diesel generator set supplies 1500 rpm 300 kva Supplying and installing Diesel generator set supplies 1500 rpm 300 kva as per the requirements in technical specifications. These technical specifications describe the Electrogen Group with 1 piece of 300 kVA standby / 300 kVA prime Diesel-Cabin and ATS Panel, which automatically go and charge itself with totally 300 kVA stand-by load in 0-7 seconds, when the city network power that supplies the building is disrupted, a phase is lost or the voltage or frequency goes out of the normal limits. 1 piece of Diesel-Electrogen Group with 300 kVA PRIME / 300 kVA STANDBY output power will be installed. This group being designed according to the applicable standards of ANSI, NEC, ISO, UL, IEEE and NEMA, its power will be determined, and being tested, will be packaged. The diesel generator set shall be manufactured by a manufacturer with ISO 9001 quality assurance certificate. Electrogen group; consists of the diesel engine, the alternator directly driven by the engine as well as type force, control, protection panels which are mounted in separate place. The Diesel - Generator set shall be combined by directly coupling on a common chassis. All parts and materials used in the generator group shall be unused. Generator Set Specifications Prime Net Power : 256 ekW / 300 kVA Standby Net Power : 256 ekW / 300 kVA Alternator Output Voltage: 400 Volts / 3 phases Frequency / Rotation : 50 Hz / 1500 rpm. Power Factor : 0.8 Voltage Regulation : + - 0.5% Waveform NEMA : 50 Wave Form IEC :% 2 Total Harmonic Content: 4% (LL /LN) All necessary materials including losses, transportation to site together with all relevant materials, installation and mounting, commissioning, testing, workmanship, contractor’s profit and general expenses for functional delivery of the item is included in this unit price. This price is per pcs Shall read as new text: PRICE No : EW-RC-GNR-01-018 Title : Diesel generator set supplies 1500 rpm 300 kva Supplying and installing Diesel generator set supplies 1500 rpm 300 kva as per the requirements in technical specifications. These technical specifications describe the Electrogen Group with 1 piece of 300 kVA standby / 300 kVA prime Diesel-Cabin and ATS Panel, which automatically go and charge itself with totally 300 kVA stand-by load in 0-7 seconds, when the city network power that supplies the building is disrupted, a phase is lost or the voltage or frequency goes out of the normal limits. 1 piece of Diesel-Electrogen Group with 300 kVA PRIME / 300 kVA STANDBY output power will be installed. This group being designed according to the applicable standards of ANSI, NEC, ISO, UL, IEEE and NEMA, its power will be determined, and being tested, will be packaged. The diesel generator set shall be manufactured by a manufacturer with ISO 9001 quality assurance certificate. Electrogen group; consists of the diesel engine, the alternator directly driven by the engine as well as type force, control, protection panels which are mounted in separate place. The Diesel - Generator set shall be combined by directly coupling on a common chassis. All parts and materials used in the generator group shall be unused. Generator Set Specifications Prime Net Power : 256 ekW / 300 kVA Standby Net Power : 256 ekW / 300 kVA Alternator Output Voltage: 400 Volts / 3 phases Frequency / Rotation : 50 Hz / 1500 rpm. Power Factor : 0.8 Voltage Regulation : + - 0.5% Waveform NEMA : 50 Wave Form IEC :% 2 Total Harmonic Content: 4% (LL /LN) New fuel tank will be provided for the generator and it is included in the unit price. Fuel Tank shall be double walled, manufactured from ST 37-2 carbon steel and according to TSE EN 12285-1 and 2. The tanks will also be insulated taking into account weather conditions of the locations to be installed. The fuel reservoir need to have a capacity sufficient for running for at least 11 hours at 100% load. The generator will be delivered with full tank and fuel costs will also be included in the unit price. The generator will be placed outside and a cabin will be installed. The cabin cover shall be at least 1.8 mm thick galvanised sheets with dimensions conforming with the generator proposed by the Contractor. The cabin shall be waterproof. The walls shall be electrostatic powder painted. The cabin shall have lockable doors. The cabin shall also be insulated with inflammable material. The cabin shall also be placed on a reinforced concrete block at least 30 cm above the ground level. All the works included above shall be included in the unit price of the generator. All necessary materials including losses, transportation to site together with all relevant materials, installation and mounting, commissioning, testing, workmanship, contractor’s profit and general expenses for functional delivery of the item is included in this unit price. This price is per pcs EW-RC-FAAS-01-001 The former text: PRICE No : EW-RC-FAAS-01-001 Title : 1 cycle, 12 zones Intelligent analogue addressed fire alarm control panel with 127 address capacity 1 cycle, 12 zones 127 address capacity analog address fire alarm control panel. Shall comply with TS EN 54-2 and TS EN 54-4. Supplying main control central together with power supply, accumulator, printer operator terminal etc. Installing, preparing software programme, connecting central with other systems, engaging the system and all tests are included. All necessary materials including losses, transportation to site together with all relevant materials, installation and mounting, commissioning, testing, workmanship, contractor’s profit and general expenses for functional delivery of the item is included in this unit price. This price is per pieces installed. Shall read as new text: PRICE No : EW-RC-FAAS-01-001 Title : 1 cycle, 12 zones Intelligent analogue addressed fire alarm control panel with 127 address capacity 1 cycle, 12 zones 127 address capacity analog address fire alarm control panel. Shall comply with TS EN 54-2 and TS EN 54-4. Supplying main control central together with power supply, accumulator, printer operator terminal etc. Installing, preparing software programme, connecting central with other systems, engaging the system and all tests are included. All necessary materials including losses, transportation to site together with all relevant materials, installation and mounting, commissioning, testing, workmanship, contractor’s profit and general expenses for functional delivery of the item is included in this unit price. Disassembling of the existing items for Fire Alarm System will be also be carried out by the Contractor and they are also included in the unit price. This price is per pieces installed. EW-RC-FAAS-01-002 The former text: PRICE No : EW-RC-FAAS-01-002 Title : Optical smoke detector with analogue address Detectors should be sensitive to the smoke particles which are sized between 0.5 and 10 microns. Detector should have double-cubicle ionization cell to be not affected from dampness, warmth etc. While the detector, the analog smoke levels measured as analog information to the control panel, the values such as calibration, performance, sensitivity should be sent to test the control panel over a cable. At least one LED indicator should be found on detector to support the controlling of detector from a distance and the indicator should be appropriate with parallel warning lamp connection. Detector should be mounted and demounted easily via specific socket. The addressing of detector should be done with any location key or hand-type programmer type device. Detector shall comply with TS EN 54-7 and the manufacturer of detector should have ISO 9001 quality guarantee certificate. The detector should be delivered to the working place in operating condition with every kind of secondary materials. Supplying optic smoke detector, connecting to the fire alarm sorties included. Socket shall be attached to the base type detector. All necessary materials including losses, transportation to site together with all relevant materials, installation and mounting, commissioning, testing, workmanship, contractor’s profit and general expenses for functional delivery of the item is included in this unit price. This price is per pieces installed. Shall read as new text: PRICE No : EW-RC-FAAS-01-002 Title : Optical smoke detector with analogue address Detectors should be sensitive to the smoke particles which are sized between 0.5 and 10 microns. Detector should have double-cubicle ionization cell to be not affected from dampness, warmth etc. While the detector, the analog smoke levels measured as analog information to the control panel, the values such as calibration, performance, sensitivity should be sent to test the control panel over a cable. At least one LED indicator should be found on detector to support the controlling of detector from a distance and the indicator should be appropriate with parallel warning lamp connection. Detector should be mounted and demounted easily via specific socket. The addressing of detector should be done with any location key or hand-type programmer type device. Detector shall comply with TS EN 54-7 and the manufacturer of detector should have ISO 9001 quality guarantee certificate. The detector should be delivered to the working place in operating condition with every kind of secondary materials. Supplying optic smoke detector, connecting to the fire alarm sorties included. Socket shall be attached to the base type detector. All necessary materials including losses, transportation to site together with all relevant materials, installation and mounting, commissioning, testing, workmanship, contractor’s profit and general expenses for functional delivery of the item is included in this unit price. Disassembling of the existing items for Fire Alarm System will be also be carried out by the Contractor and they are also included in the unit price. This price is per pieces installed. EW-RC-FAAS-01-003 The former text: PRICE No : EW-RC-FAAS-01-003 Title : Gas detector with Intelligent analogue address Supplying explosive gas detector as per the requirements in technical specifications, connecting to the fire alarm sorties included. Socket shall be attached to the base type detector. All necessary materials including losses, transportation to site together with all relevant materials, installation and mounting, commissioning, testing, workmanship, contractor’s profit and general expenses for functional delivery of the item is included in this unit price. This price is per pieces installed. Shall read as new text: PRICE No : EW-RC-FAAS-01-003 Title : Gas detector with Intelligent analogue address Supplying explosive gas detector as per the requirements in technical specifications, connecting to the fire alarm sorties included. Socket shall be attached to the base type detector. All necessary materials including losses, transportation to site together with all relevant materials, installation and mounting, commissioning, testing, workmanship, contractor’s profit and general expenses for functional delivery of the item is included in this unit price. Disassembling of the existing items for Fire Alarm System will be also be carried out by the Contractor and they are also included in the unit price. This price is per pieces installed. EW-RC-FAAS-01-004 The former text: PRICE No : EW-RC-FAAS-01-004 Title : Fire alarm button with analogue address Addressable fire alarm buttons shall be activated by breaking the plastic film coated glass over the button. When glass is broken, micro switch shall be in free position and kept in this position until a new glass is installed. Button shall be tested by a test switch without breaking the glass. At least one pieces of indicator with light shall exist over the button. Button shall comply with TS EN 54-2. All necessary fittings and accessories included. Supplying fire alarm button, connecting to the fire alarm sorties All necessary materials including losses, transportation to site together with all relevant materials, installation and mounting, commissioning, testing, workmanship, contractor’s profit and general expenses for functional delivery of the item is included in this unit price. This price is per pieces installed. Shall read as new text: PRICE No : EW-RC-FAAS-01-004 Title : Fire alarm button with analogue address Addressable fire alarm buttons shall be activated by breaking the plastic film coated glass over the button. When glass is broken, micro switch shall be in free position and kept in this position until a new glass is installed. Button shall be tested by a test switch without breaking the glass. At least one pieces of indicator with light shall exist over the button. Button shall comply with TS EN 54-2. All necessary fittings and accessories included. Supplying fire alarm button, connecting to the fire alarm sorties All necessary materials including losses, transportation to site together with all relevant materials, installation and mounting, commissioning, testing, workmanship, contractor’s profit and general expenses for functional delivery of the item is included in this unit price. Disassembling of the existing items for Fire Alarm System will be also be carried out by the Contractor and they are also included in the unit price. This price is per pieces installed. EW-RC-FAAS-01-005 The former text: PRICE No : EW-RC-FAAS-01-005 Title : Strobed Fire alarm system with Intelligent analogue address-Online feed Indoor type fire alarm siren shall have minimum 100 db/1mt sound intensity and 32 different tunes. It shall be minimum IP44. It shall comply with TS EN 54-3 and ISO 9001. All necessary fittings and accessories included. Supplying regular type siren. All necessary materials including losses, transportation to site together with all relevant materials, installation and mounting, commissioning, testing, workmanship, contractor’s profit and general expenses for functional delivery of the item is included in this unit price. This price is per pieces installed. Shall read as new text: PRICE No : EW-RC-FAAS-01-005 Title : Strobed Fire alarm system with Intelligent analogue address-Online feed Indoor type fire alarm siren shall have minimum 100 db/1mt sound intensity and 32 different tunes. It shall be minimum IP44. It shall comply with TS EN 54-3 and ISO 9001. All necessary fittings and accessories included. Supplying regular type siren. All necessary materials including losses, transportation to site together with all relevant materials, installation and mounting, commissioning, testing, workmanship, contractor’s profit and general expenses for functional delivery of the item is included in this unit price. Disassembling of the existing items for Fire Alarm System will be also be carried out by the Contractor and they are also included in the unit price. This price is per pieces installed. EW-RC-FAAS-01-006 The former text: PRICE No : EW-RC-FAAS-01-006 Title : Contact monitoring module with Intelligent analog address Contact monitoring module with Intelligent analog address as per the requirements in technical specifications. All necessary materials including losses, transportation to site together with all relevant materials, installation and mounting, commissioning, testing, workmanship, contractor’s profit and general expenses for functional delivery of the item is included in this unit price. This price is per pcs Shall read as new text: PRICE No : EW-RC-FAAS-01-006 Title : Contact monitoring module with Intelligent analog address Contact monitoring module with Intelligent analog address as per the requirements in technical specifications. All necessary materials including losses, transportation to site together with all relevant materials, installation and mounting, commissioning, testing, workmanship, contractor’s profit and general expenses for functional delivery of the item is included in this unit price. Disassembling of the existing items for Fire Alarm System will be also be carried out by the Contractor and they are also included in the unit price. This price is per pcs EW-RC-FAAS-01-007 The former text: PRICE No : EW-RC-FAAS-01-007 Title : An hour Emergency guidance luminaire An hour Emergency guidance luminaire as per the requirements in technical specifications. All necessary materials including losses, transportation to site together with all relevant materials, installation and mounting, commissioning, testing, workmanship, contractor’s profit and general expenses for functional delivery of the item is included in this unit price. This price is per pcs Shall read as new text: PRICE No : EW-RC-FAAS-01-007 Title : An hour Emergency guidance luminaire An hour Emergency guidance luminaire as per the requirements in technical specifications. All necessary materials including losses, transportation to site together with all relevant materials, installation and mounting, commissioning, testing, workmanship, contractor’s profit and general expenses for functional delivery of the item is included in this unit price. Disassembling of the existing items for Fire Alarm System will be also be carried out by the Contractor and they are also included in the unit prices. This price is per pcs EW-RC-FAAS-01-008 The former text: PRICE No : EW-RC-FAAS-01-008 Title : Cable feeder with Lead-free pvc insulated (nhxmh) - 3x2.5 Cable feeder with Lead-free pvc insulated (nhxmh) - 3x2.5. All necessary materials including losses, transportation to site together with all relevant materials, installation and mounting, commissioning, testing, workmanship, contractor’s profit and general expenses for functional delivery of the item is included in this unit price. This price is per m Shall read as new text: PRICE No : EW-RC-FAAS-01-008 Title : Cable feeder with Lead-free pvc insulated (nhxmh) - 3x2.5 Cable feeder with Lead-free pvc insulated (nhxmh) - 3x2.5. All necessary materials including losses, transportation to site together with all relevant materials, installation and mounting, commissioning, testing, workmanship, contractor’s profit and general expenses for functional delivery of the item is included in this unit price. Disassembling of the existing items for Fire Alarm System will be also be carried out by the Contractor and they are also included in the unit prices. This price is per m EW-RC-FAAS-01-009 The former text: PRICE No : EW-RC-FAAS-01-009 Title : Jh (st) Halogen-free fire alarm cabling 2x2x0.8+0.8 mm2 Supplying cable, installing inside cable carriers or halogen free passing and security pipes, antigron junction box are included. All crochets, crochet bridges, electric terminals, attaching labels, making cable end connections. All necessary materials including losses, transportation to site together with all relevant materials, installation and mounting, commissioning, testing, workmanship, contractor’s profit and general expenses for functional delivery of the item is included in this unit price. This price is per meter of cable laid. Shall read as new text: PRICE No : EW-RC-FAAS-01-009 Title : Jh (st) Halogen-free fire alarm cabling 2x2x0.8+0.8 mm2 Supplying cable, installing inside cable carriers or halogen free passing and security pipes, antigron junction box are included. All crochets, crochet bridges, electric terminals, attaching labels, making cable end connections. All necessary materials including losses, transportation to site together with all relevant materials, installation and mounting, commissioning, testing, workmanship, contractor’s profit and general expenses for functional delivery of the item is included in this unit price. Disassembling of the existing items for Fire Alarm System will be also be carried out by the Contractor and they are also included in the unit prices. This price is per meter of cable laid. EW-RC-FAAS-01-010 The former text: PRICE No : EW-RC-FAAS-01-010 Title : 2 cycle, 24 zones Intelligent analogue addressed fire alarm control panel with 127 address capacity. 2 cycle, 24 zones 127 address capacity analog address fire alarm control panel. Shall comply with TS EN 54-2 and TS EN 54-4. Supplying main control central together with power supply, accumulator, printer operator terminal etc. Installing, preparing software programme, connecting central with other systems, engaging the system and all tests are included. All necessary materials including losses, transportation to site together with all relevant materials, installation and mounting, commissioning, testing, workmanship, contractor’s profit and general expenses for functional delivery of the item is included in this unit price. This price is per pcs Shall read as new text: PRICE No : EW-RC-FAAS-01-010 Title : 2 cycle, 24 zones Intelligent analogue addressed fire alarm control panel with 127 address capacity. 2 cycle, 24 zones 127 address capacity analog address fire alarm control panel. Shall comply with TS EN 54-2 and TS EN 54-4. Supplying main control central together with power supply, accumulator, printer operator terminal etc. Installing, preparing software programme, connecting central with other systems, engaging the system and all tests are included. All necessary materials including losses, transportation to site together with all relevant materials, installation and mounting, commissioning, testing, workmanship, contractor’s profit and general expenses for functional delivery of the item is included in this unit price. Disassembling of the existing items for Fire Alarm System will be also be carried out by the Contractor and they are also included in the unit prices. This price is per pcs EW-RC-FAAS-01-011 The former text: PRICE No : EW-RC-FAAS-01-011 Title : Combined analogue address Temperature detector Combined analogue address Temperature detector as per the requirements in technical specifications. All necessary materials including losses, transportation to site together with all relevant materials, installation and mounting, commissioning, testing, workmanship, contractor’s profit and general expenses for functional delivery of the item is included in this unit price. This price is per pcs Shall read as new text: PRICE No : EW-RC-FAAS-01-011 Title : Combined analogue address Temperature detector Combined analogue address Temperature detector as per the requirements in technical specifications. All necessary materials including losses, transportation to site together with all relevant materials, installation and mounting, commissioning, testing, workmanship, contractor’s profit and general expenses for functional delivery of the item is included in this unit price. Disassembling of the existing items for Fire Alarm System will be also be carried out by the Contractor and they are also included in the unit prices. This price is per pcs EW-RC-CCTV-01-001 The former text: PRICE No : EW-RC-CCTV-01-001 Title : Utp cat6 cable With 250 Mhz bandwidth. With 4-pairs and 4 colour codes with 250 Mbps data communication capacity including PVC outer sheath, 4 Double Cable, 23 AWG standard with 0.57 mm bare copper coating. Shall be compatible with TS EN 50288-3-1,2, ISO 11801 standards. Supplying cable, installing inside cable carriers or halogen free passing and security pipes, antigron junction box are included. All crochets, crochet bridges, electric terminals, attaching labels, making cable end connections. All necessary materials including losses, transportation to site together with all relevant materials, installation and mounting, commissioning, testing, workmanship, contractor’s profit and general expenses for functional delivery of the item is included in this unit price. This price is per m Shall read as new text: PRICE No : EW-RC-CCTV-01-001 Title : Utp cat6 cable With 250 Mhz bandwidth. With 4-pairs and 4 colour codes with 250 Mbps data communication capacity including PVC outer sheath, 4 Double Cable, 23 AWG standard with 0.57 mm bare copper coating. Shall be compatible with TS EN 50288-3-1,2, ISO 11801 standards. Supplying cable, installing inside cable carriers or halogen free passing and security pipes, antigron junction box are included. All crochets, crochet bridges, electric terminals, attaching labels, making cable end connections. All necessary materials including losses, transportation to site together with all relevant materials, installation and mounting, commissioning, testing, workmanship, contractor’s profit and general expenses for functional delivery of the item is included in this unit price. Disassembling of the existing items for CCTV System will be also be carried out by the Contractor and they are also included in the unit prices. This price is per m EW-RC-CCTV-01-002 The former text: PRICE No : EW-RC-CCTV-01-002 Title : Standing type cabinets - 15u 600 mm * 600 mm 19" Supply of the 600mm x 600 mm 19” Standing Type Rack Cabinet with brake wheels, fan groups, socket groups, thermostat, etc. as mentioned in the specifications. With min. inner mast and back cover in 2 mm thickness; inner surfaces of the cabin made of DKP plate with a thickness of at least 1.5 mm. With min. 19 "wide sewing gaps. With wheels (capable of carrying loads of at least 200 kg). With ability to stabilize cables. With rear covers and inner stitches (2 at the front and 2 at the rear). Bottom chasses of the cabinets, provided with the capability of a dust ingress preventive cable entry section and of fixation of cables, front, rear and side covers of the cabinets provided with key lock openable and dismountable, front covers of the cabinets, in order to reinforce the strength of the front cover pane, tempered, antistatic, secure, smoke-colored, running-in min. 4 mm thick glass and at least at 135 degrees key-lock openable, dismountable; at least 3 cm. wide screwed, metal inserted, frame structure holding the glass around the pane; painted with electrostatic powder paint, at the upper part of the cabinets and/or on the side surfaces are provided with air venting holes, upper cover and/or when the cap is dismounted it is so designed to intervene to the fan group, each one of the square holes, one side of which is 9,5±0.01 mm on the cabinet struts; cabinet struts shall be capable of moving along the depth of cabins. All necessary materials including losses, transportation to site together with all relevant materials, installation and mounting, commissioning, testing, workmanship, contractor’s profit and general expenses for functional delivery of the item is included in this unit price. This price is per piece installed. Shall read as new text: PRICE No : EW-RC-CCTV-01-002 Title : Standing type cabinets - 15u 600 mm * 600 mm 19" Supply of the 600mm x 600 mm 19” Standing Type Rack Cabinet with brake wheels, fan groups, socket groups, thermostat, etc. as mentioned in the specifications. With min. inner mast and back cover in 2 mm thickness; inner surfaces of the cabin made of DKP plate with a thickness of at least 1.5 mm. With min. 19 "wide sewing gaps. With wheels (capable of carrying loads of at least 200 kg). With ability to stabilize cables. With rear covers and inner stitches (2 at the front and 2 at the rear). Bottom chasses of the cabinets, provided with the capability of a dust ingress preventive cable entry section and of fixation of cables, front, rear and side covers of the cabinets provided with key lock openable and dismountable, front covers of the cabinets, in order to reinforce the strength of the front cover pane, tempered, antistatic, secure, smoke-colored, running-in min. 4 mm thick glass and at least at 135 degrees key-lock openable, dismountable; at least 3 cm. wide screwed, metal inserted, frame structure holding the glass around the pane; painted with electrostatic powder paint, at the upper part of the cabinets and/or on the side surfaces are provided with air venting holes, upper cover and/or when the cap is dismounted it is so designed to intervene to the fan group, each one of the square holes, one side of which is 9,5±0.01 mm on the cabinet struts; cabinet struts shall be capable of moving along the depth of cabins. All necessary materials including losses, transportation to site together with all relevant materials, installation and mounting, commissioning, testing, workmanship, contractor’s profit and general expenses for functional delivery of the item is included in this unit price. Disassembling of the existing items for CCTV System will be also be carried out by the Contractor and they are also included in the unit prices. This price is per piece installed. EW-RC-CCTV-01-003 The former text: PRICE No : EW-RC-CCTV-01-003 Title : Patch panel with 24 ports utp cat6 Min. 100 Mhz band width, Min. 100 Mbps. 4 per, 4 colour code. Unarmed, twisted pers. PVC outside shielding covers all wires, Ended with 26 AWG 7x0,16 mm bare copper. Comply with ANSI/TIA/EIA-568, TS EN 50288-3, TS ISO/IEC 11801. Supplying the patch panel. All necessary materials including losses, transportation to site together with all relevant materials, installation and mounting, commissioning, testing, workmanship, contractor’s profit and general expenses for functional delivery of the item is included in this unit price. This price is per pcs Shall read as new text: PRICE No : EW-RC-CCTV-01-003 Title : Patch panel with 24 ports utp cat6 Min. 100 Mhz band width, Min. 100 Mbps. 4 per, 4 colour code. Unarmed, twisted pers. PVC outside shielding covers all wires, Ended with 26 AWG 7x0,16 mm bare copper. Comply with ANSI/TIA/EIA-568, TS EN 50288-3, TS ISO/IEC 11801. Supplying the patch panel. All necessary materials including losses, transportation to site together with all relevant materials, installation and mounting, commissioning, testing, workmanship, contractor’s profit and general expenses for functional delivery of the item is included in this unit price. Disassembling of the existing items for CCTV System will be also be carried out by the Contractor and they are also included in the unit prices. This price is per pcs EW-RC-CCTV-01-004 The former text: PRICE No : EW-RC-CCTV-01-004 Title : Brake wheel group (accessory) Braked wheel group (accessory) for cabinets. All necessary materials including losses, transportation to site together with all relevant materials, installation and mounting, commissioning, testing, workmanship, contractor’s profit and general expenses for functional delivery of the item is included in this unit price. This price is per pcs Shall read as new text: PRICE No : EW-RC-CCTV-01-004 Title : Brake wheel group (accessory) Braked wheel group (accessory) for cabinets. All necessary materials including losses, transportation to site together with all relevant materials, installation and mounting, commissioning, testing, workmanship, contractor’s profit and general expenses for functional delivery of the item is included in this unit price. Disassembling of the existing items for CCTV System will be also be carried out by the Contractor and they are also included in the unit prices. This price is per pcs EW-RC-CCTV-01-005 The former text: PRICE No : EW-RC-CCTV-01-005 Title : 1000 mm Fixed shelf (accessory) 1000 mm Fixed shelf (accessory) for cabinets. All necessary materials including losses, transportation to site together with all relevant materials, installation and mounting, commissioning, testing, workmanship, contractor’s profit and general expenses for functional delivery of the item is included in this unit price. This price is per pcs Shall read as new text: PRICE No : EW-RC-CCTV-01-005 Title : 1000 mm Fixed shelf (accessory) 1000 mm Fixed shelf (accessory) for cabinets. All necessary materials including losses, transportation to site together with all relevant materials, installation and mounting, commissioning, testing, workmanship, contractor’s profit and general expenses for functional delivery of the item is included in this unit price. Disassembling of the existing items for CCTV System will be also be carried out by the Contractor and they are also included in the unit prices. This price is per pcs EW-RC-CCTV-01-006 The former text: PRICE No : EW-RC-CCTV-01-006 Title : 1000 mm movable shelf (accessory) 1000 mm movable shelf (accessory) for cabinets. All necessary materials including losses, transportation to site together with all relevant materials, installation and mounting, commissioning, testing, workmanship, contractor’s profit and general expenses for functional delivery of the item is included in this unit price. This price is per pcs Shall read as new text: PRICE No : EW-RC-CCTV-01-006 Title : 1000 mm movable shelf (accessory) 1000 mm movable shelf (accessory) for cabinets. All necessary materials including losses, transportation to site together with all relevant materials, installation and mounting, commissioning, testing, workmanship, contractor’s profit and general expenses for functional delivery of the item is included in this unit price. Disassembling of the existing items for CCTV System will be also be carried out by the Contractor and they are also included in the unit prices. This price is per pcs EW-RC-CCTV-01-007 The former text: PRICE No : EW-RC-CCTV-01-007 Title : 15u Vertical cable organizer Supplying the vertical cable organizer for data rack cabinets. All necessary materials including losses, transportation to site together with all relevant materials, installation and mounting, commissioning, testing, workmanship, contractor’s profit and general expenses for functional delivery of the item is included in this unit price. This price is per pieces installed. Shall read as new text: PRICE No : EW-RC-CCTV-01-007 Title : 15u Vertical cable organizer Supplying the vertical cable organizer for data rack cabinets. All necessary materials including losses, transportation to site together with all relevant materials, installation and mounting, commissioning, testing, workmanship, contractor’s profit and general expenses for functional delivery of the item is included in this unit price. Disassembling of the existing items for CCTV System will be also be carried out by the Contractor and they are also included in the unit prices. This price is per pieces installed. EW-RC-CCTV-01-008 The former text: PRICE No : EW-RC-CCTV-01-008 Title : Thermostatic fan module (with 4 fans) Supplying the fan module with thermostat for data rack cabinets. All necessary materials including losses, transportation to site together with all relevant materials, installation and mounting, commissioning, testing, workmanship, contractor’s profit and general expenses for functional delivery of the item is included in this unit price. This price is per pieces installed. Shall read as new text: PRICE No : EW-RC-CCTV-01-008 Title : Thermostatic fan module (with 4 fans) Supplying the fan module with thermostat for data rack cabinets. All necessary materials including losses, transportation to site together with all relevant materials, installation and mounting, commissioning, testing, workmanship, contractor’s profit and general expenses for functional delivery of the item is included in this unit price. Disassembling of the existing items for CCTV System will be also be carried out by the Contractor and they are also included in the unit prices. This price is per pieces installed. EW-RC-CCTV-01-009 The former text: PRICE No : EW-RC-CCTV-01-009 Title : 19" rack type with 6 groups of plug (braker) Supplying the rack type switched socket group of 6 sockets for data rack cabinets. All necessary materials including losses, transportation to site together with all relevant materials, installation and mounting, commissioning, testing, workmanship, contractor’s profit and general expenses for functional delivery of the item is included in this unit price. This price is per pieces installed. Shall read as new text: PRICE No : EW-RC-CCTV-01-009 Title : 19" rack type with 6 groups of plug (braker) Supplying the rack type switched socket group of 6 sockets for data rack cabinets. All necessary materials including losses, transportation to site together with all relevant materials, installation and mounting, commissioning, testing, workmanship, contractor’s profit and general expenses for functional delivery of the item is included in this unit price. Disassembling of the existing items for CCTV System will be also be carried out by the Contractor and they are also included in the unit prices. This price is per pieces installed. EW-RC-CCTV-01-010 The former text: PRICE No : EW-RC-CCTV-01-010 Title : 19" 1u Horizontal cable organizer Supplying the 19” Horizontal cable organizer for data rack cabinets. All necessary materials including losses, transportation to site together with all relevant materials, installation and mounting, commissioning, testing, workmanship, contractor’s profit and general expenses for functional delivery of the item is included in this unit price. This price is per pieces installed. Shall read as new text: PRICE No : EW-RC-CCTV-01-010 Title : 19" 1u Horizontal cable organizer Supplying the 19” Horizontal cable organizer for data rack cabinets. All necessary materials including losses, transportation to site together with all relevant materials, installation and mounting, commissioning, testing, workmanship, contractor’s profit and general expenses for functional delivery of the item is included in this unit price. Disassembling of the existing items for CCTV System will be also be carried out by the Contractor and they are also included in the unit prices. This price is per pieces installed. EW-RC-CCTV-01-011 The former text: PRICE No : EW-RC-CCTV-01-011 Title : Internal Fixed Camera Supplying internal Fixed Camera as per the requirements in technical specifications, electric terminals, attaching labels, making cable end connections. All necessary materials including losses, transportation to site together with all relevant materials, installation and mounting, commissioning, testing, workmanship, contractor’s profit and general expenses for functional delivery of the item is included in this unit price. This price is per piece installed. Shall read as new text: PRICE No : EW-RC-CCTV-01-011 Title : Internal Fixed Camera Supplying internal Fixed Camera as per the requirements in technical specifications, electric terminals, attaching labels, making cable end connections. All necessary materials including losses, transportation to site together with all relevant materials, installation and mounting, commissioning, testing, workmanship, contractor’s profit and general expenses for functional delivery of the item is included in this unit price. Disassembling of the existing items for CCTV System will be also be carried out by the Contractor and they are also included in the unit prices. This price is per piece installed. EW-RC-CCTV-01-012 The former text: PRICE No : EW-RC-CCTV-01-012 Title : External Fixed Camera Supplying and installing external Fixed Camera as per the requirements in technical specifications, electric terminals, attaching labels, making cable end connections. All necessary materials including losses, transportation to site together with all relevant materials, installation and mounting, commissioning, testing, workmanship, contractor’s profit and general expenses for functional delivery of the item is included in this unit price. This price is per piece installed. Shall read as new text: PRICE No : EW-RC-CCTV-01-012 Title : External Fixed Camera Supplying and installing external Fixed Camera as per the requirements in technical specifications, electric terminals, attaching labels, making cable end connections. All necessary materials including losses, transportation to site together with all relevant materials, installation and mounting, commissioning, testing, workmanship, contractor’s profit and general expenses for functional delivery of the item is included in this unit price. Disassembling of the existing items for CCTV System will be also be carried out by the Contractor and they are also included in the unit prices. This price is per piece installed. EW-RC-CCTV-01-013 The former text: PRICE No : EW-RC-CCTV-01-013 Title : 32 Channels capacity Digital Recorders Supplying and installing 32 Channels capacity Digital Recorders as per the requirements in technical specifications. All necessary materials including losses, transportation to site together with all relevant materials, installation and mounting, commissioning, testing, workmanship, contractor’s profit and general expenses for functional delivery of the item is included in this unit price. This price is per pcs Shall read as new text: PRICE No : EW-RC-CCTV-01-013 Title : 32 Channels capacity Digital Recorders Supplying and installing 32 Channels capacity Digital Recorders as per the requirements in technical specifications. All necessary materials including losses, transportation to site together with all relevant materials, installation and mounting, commissioning, testing, workmanship, contractor’s profit and general expenses for functional delivery of the item is included in this unit price. Disassembling of the existing items for CCTV System will be also be carried out by the Contractor and they are also included in the unit prices. This price is per pcs EW-RC-CCTV-01-014 The former text: PRICE No : EW-RC-CCTV-01-014 Title : 24 PORT POE SWITCH .Supplying and installing 24 PORT POE SWITCH as per the requirements in technical specifications. All necessary materials including losses, transportation to site together with all relevant materials, installation and mounting, commissioning, testing, workmanship, contractor’s profit and general expenses for functional delivery of the item is included in this unit price. This price is per pieces installed. Shall read as new text: PRICE No : EW-RC-CCTV-01-014 Title : 24 PORT POE SWITCH .Supplying and installing 24 PORT POE SWITCH as per the requirements in technical specifications. All necessary materials including losses, transportation to site together with all relevant materials, installation and mounting, commissioning, testing, workmanship, contractor’s profit and general expenses for functional delivery of the item is included in this unit price. Disassembling of the existing items for CCTV System will be also be carried out by the Contractor and they are also included in the unit prices. This price is per pieces installed. EW-RC-CCTV-01-015 The former text: PRICE No : EW-RC-CCTV-01-015 Title : 23 '' Monitor Supply of 23” TFT-LCD Monitor as per the requirements in technical specifications. Vertical resolution in pixel is 1080. Horizontal resolution in pixel will be 1920. All necessary materials including losses, transportation to site together with all relevant materials, installation and mounting, commissioning, testing, workmanship, contractor’s profit and general expenses for functional delivery of the item is included in this unit price. This price is per pieces installed. Shall read as new text: PRICE No : EW-RC-CCTV-01-015 Title : 23 '' Monitor Supply of 23” TFT-LCD Monitor as per the requirements in technical specifications. Vertical resolution in pixel is 1080. Horizontal resolution in pixel will be 1920. All necessary materials including losses, transportation to site together with all relevant materials, installation and mounting, commissioning, testing, workmanship, contractor’s profit and general expenses for functional delivery of the item is included in this unit price. Disassembling of the existing items for CCTV System will be also be carried out by the Contractor and they are also included in the unit prices. This price is per pieces installed. EW-RC-CCTV-01-016 The former text: PRICE No : EW-RC-CCTV-01-016 Title : 2TB HDD Supplying and installing 2TB HDD as per the requirements in technical specifications. All necessary materials including losses, transportation to site together with all relevant materials, installation and mounting, commissioning, testing, workmanship, contractor’s profit and general expenses for functional delivery of the item is included in this unit price. This price is per pcs Shall read as new text: PRICE No : EW-RC-CCTV-01-016 Title : 2TB HDD Supplying and installing 2TB HDD as per the requirements in technical specifications. All necessary materials including losses, transportation to site together with all relevant materials, installation and mounting, commissioning, testing, workmanship, contractor’s profit and general expenses for functional delivery of the item is included in this unit price. Disassembling of the existing items for CCTV System will be also be carried out by the Contractor and they are also included in the unit prices. This price is per pcs EW-RC-CCTV-01-017 The former text: PRICE No : EW-RC-CCTV-01-017 Title : 48 PORT POE SWITCH Supplying and installing 48 PORT POE SWITCH as per the requirements in technical specifications. All necessary materials including losses, transportation to site together with all relevant materials, installation and mounting, commissioning, testing, workmanship, contractor’s profit and general expenses for functional delivery of the item is included in this unit price. This price is per pcs Shall read as new text: PRICE No : EW-RC-CCTV-01-017 Title : 48 PORT POE SWITCH Supplying and installing 48 PORT POE SWITCH as per the requirements in technical specifications. All necessary materials including losses, transportation to site together with all relevant materials, installation and mounting, commissioning, testing, workmanship, contractor’s profit and general expenses for functional delivery of the item is included in this unit price. Disassembling of the existing items for CCTV System will be also be carried out by the Contractor and they are also included in the unit prices. This price is per pcs The Price Schedules for following items are removed since related works are removed from scope. PRICE No : CW-TR-RC-025 Title : Entrance system with card reader Entrance system with card reader including Digital Keypad, Weather & Vandal Resistant Housing with Metal Keys, Dual LED Status Indicators, Configurable Illumination. All kind of materials for construction, workshop expenses, vertical and horizontal transportation in the workplace, unloading, workmanship, contractor’s general expenses and profit is included. This price is per pcs PRICE No : MW-RC-SAS-01-001 Title : Solar Collector with selective surface Solar Collectors with selective surface shall be installed as per the requirements in technical specifications. All kind of materials for construction, workshop expenses, vertical and horizontal transportation in the workplace, unloading, workmanship, contractor’s general expenses and profit is included. This price is per m² PRICE No : MW-RC-SAS-01-005 Title : 10,00 m3 stainless steel water tank - prismatic modules All made of AISI 304 stainless steel, all internal materials, external materials, tension rods, bolts, foot, manhole, air-valves and fitting ports made of stainless steel, fixtures thereon made of either stainless steel or brass materials, its resistance calculations and projects provided, all components were produced under the factory conditions by means of cold forming, bending or twisting method; PVC or polyethylene diaphragm to cut the connection of the base material at the base of the tank which was joined with bolts using silicon and epidemic rubber seals without requiring any welding operation at its production and assembly site of the Modular Water Tank provided with Turkish Standards Conformity Certificate is to be supplied at the worksite and its installation at the required location after connecting to the existing water supply system. Note: Armatures made of stainless steel or chromizing brass material available on the Tank, stainless steel tank foot, level floater, input-output spherical/globe valves, globe blowdown valves, air bleed valve ventilator, tank overflow mouth and pipe, level gage, valves and discharge valve, upper and bottom manhole maintenance cover, tank climbing ladder are included in the price. All kind of materials for construction, workshop expenses, vertical and horizontal transportation in the workplace, unloading, workmanship, contractor’s general expenses and profit is included. This price is per pcs PRICE No : MW-RC-SAS-01-006 Title : Package type cold storage device (2000 kcal/h) freon 404 , hermetic compressor -15 / -25 °c (+45 °C condensation, -30 evaporation ) the refrigeration gas assembly, electrical wiring, power distribution panel, control panel, compressor, condenser and the fan motor shall be all together and these components shall be coated with electrostatic painted galvanized material so as not to be seen from outside; outer cabins of the evaporator unit and condenser unit shall be of galvanized, and visible surfaces shall be painted with electrostatic paint, in the package type cold Storage Device air-cooled condenser shall be used, evaporator’s “lamel” range shall be at 6 to 8 mm., condenser lamel range shall be between 2 mm and 3 mm.; in the cold storage device a digital cable remote controlled panel shall be present, and the device shall operate with a programmable microprocessor; the cold storage device shall be equipped with audio and light alarm system, if the room temperature does not reach at the desired level then this alarm system will emit warning; the cold storage device will protect against excessive contamination in the condenser unit or against any blockage in the system with high pressure pressure-stat by shutting the system and emit warning to the user; condenser and evaporator capacities shall be selected in conformity with the selected capacities; the supply of the package type cold storage device at the Worksite and installation of same at its place. All kind of materials for construction, workshop expenses, vertical and horizontal transportation in the workplace, unloading, workmanship, contractor’s general expenses and profit is included. This price is per pcs PRICE No : MW-RC-SAS-01-007 Title : PVC coated cold air storage doors with 12cm thick and 90 x 190 cm clear pass Supply and installation of door of the cold storage, having used 40 kg / m3 density of polyurethane as the insulation material, with door handle openable from the inside, aluminum frame, application with or without threshold. All kind of materials for construction, workshop expenses, vertical and horizontal transportation in the workplace, unloading, workmanship, contractor’s general expenses and profit is included. This price is per pcs PRICE No : MW-RC-SAS-01-008 Title : Modular type wall panel - both side are PVC coated or polyester painted and 12 cm thick Both sides coated with 0.50-0.55 mm thick hygienic material, polyurethane insulation between the galvanized sheet; density of polyurethane used as insulation material is 40-42 Kg / m3, polyurethane panels as assembled and disassembled state equipped with locking mechanism with eccentric hook; heat conductivity coefficient of polyurethane used in the insulation of the panel is k: 0.22 Kcal / hm2°C; polyurethane fire class is the self-preventive modular type cold chamber panels’ supply at the worksite and installation at their place in accordance with the international standards. Panels will be produced in accordance with TS EN 14509, pursuant to the Construction Materials Regulation no. 305/2011/AB and shall be supplied to the market using the CE sign. All kind of materials for construction, workshop expenses, vertical and horizontal transportation in the workplace, unloading, workmanship, contractor’s general expenses and profit is included. This price is per m² PRICE No : MW-RC-SAS-01-009 Title : Modular type ceiling panel - both side are PVC coated or polyester painted and 12 cm thick Both sides coated with 0.50-0.55 mm thick hygienic material, polyurethane insulation between the galvanized sheet; density of polyurethane used as insulation material is 40-42 Kg / m3, polyurethane panels as assembled and disassembled state equipped with locking mechanism with eccentric hook; heat conductivity coefficient of polyurethane used in the insulation of the panel is k: 0.22 Kcal / hm2°C; polyurethane fire class is the self-preventive modular type cold chamber panels’ supply at the worksite and installation at their place in accordance with the international standards. Panels will be produced in accordance with TS EN 14509, pursuant to the Construction Materials Regulation no. 305/2011/AB and shall be supplied to the market using the CE sign. All kind of materials for construction, workshop expenses, vertical and horizontal transportation in the workplace, unloading, workmanship, contractor’s general expenses and profit is included. This price is per m² PRICE No : MW-RC-SAS-01-010 Title : Modular type floor panel - Plywood coated and 12 cm thick Both sides coated with 0.50-0.55 mm thick hygienic material, polyurethane insulation between the galvanized sheet; density of polyurethane used as insulation material is 40-42 Kg / m3, polyurethane panels as assembled and disassembled state equipped with locking mechanism with eccentric hook; heat conductivity coefficient of polyurethane used in the insulation of the panel is k: 0.22 Kcal / hm2°C; polyurethane fire class is the self-preventive modular type cold chamber panels’ supply at the worksite and installation at their place in accordance with the international standards. Panels will be produced in accordance with TS EN 14509, pursuant to the Construction Materials Regulation no. 305/2011/AB and shall be supplied to the market using the CE sign. All kind of materials for construction, workshop expenses, vertical and horizontal transportation in the workplace, unloading, workmanship, contractor’s general expenses and profit is included. This price is per m²

All other terms and conditions of the Tender Dossier remain unchanged. The above alterations and / or corrections to the tender dossier are an integral part of the Tender Dossier.

***