CHANGES NO:4 to

TENDER DOSSIER

| Contract Title: | Construction of Removal Centres for the Effective Implementation of the EU – Turkey Readmission Agreement |
| --- | --- |
| Publication Reference: | EuropeAid/139322/IH/WKS/TR |
| Lot: | For All Lots |

The following alterations and/or corrections are made to the Tender Dossier:

VOLUME 3 TECHNICAL SPECIFICATIONS Item S.015 Add new text under the heading: The size of the fill material will be up to 2 mm. Add new item S.024A DEMOLISHING THE EXISTING CONCRETE/ASPHALT BUILDINGS, ROADS, RUNWAYS AND SIMILAR EXISTING STRUCTURES 1 m3 price of demolishing concrete/asphalt buildings, roads, runways and similar structures by machinery and equipment, loading on the vehicles and transportation and deposit on the site arranged by the Contractor in consultation with local authorities, unloading, laying or filling, filling the gaps that exists after the construction is completed and smoothing those gaps, including the cost of all material and waste, labour, tools and equipment, contractor profit and general expenditures: MEASUREMENT: In advance of demolishing, existing structures are recorded via site survey; and the volume of the demolished materials are calculated according to the dimensions of the existing structures recorded on site. Items S.026 and S.027 Add new text under the heading: The size of the fill material will be 8 mm to 32 mm. Item S.028 Add new text under the heading: The size of the fill material will be 2 mm to 5 mm. Item S.029 Add new text under the heading: The size of the blockage material will be 25 mm to 60 mm. Item S.066 Add new text under the heading: The intervals of the sunshade will be around 15-20 cm. Item S.188 Add new text under the heading: The detail drawing for the door is as follows prepared in line with the Technical Specifications: Item M.013 The former text: For use with an ; 15 mm of 15 mm chrome plated or fixed tube or plastic based (from acetal copolymer) quality certificate in accordance with TS EN 200 or TS EN 817. rechargeable battery; 6 cm from detachable type. odor-fermer, wall-extended and partly rosetted, 32 mm filter, chrome-plated brass or hard plastic based TS-EN 274-1-2-3, in accordance with the dimensions of the detachable and cleanable type at least 80 ° C temperature resistant, installation, and delivery in the work place (discharge pipe for discharge), and battery and siphon will be TS certified. Shall read as new text: One compartment sink installation; in compliance with TS EN 200 or TS EN 817, 15 mm brass chromage, rotary or fixed , fixed pipe or based plastic (made of acetal polymer) and it has quality certified, 15mm sink tap; 6cm odour fermetur, which can be removed and cleaned, extension piece up to the wall and rosette; 32 mm strainer, brass chromage, which can be dismantled and cleaned in accordance with measures of TS EN 274-1-2-3, temperature resistant to minimum 80 celsius degree; basin sink trap; delivery and installation also in the work place of bakelite sink plug, chromage chain. With faucet and brass bottle trap for basin sink which are according to TS EN 200 or TS EN 817, TS-EN 274-1-2-3 (first class). Item M.032 The former text: OPEN FIRE WATER SPRAY NOZZLE (WHITE PAINTED) Installation of an approved open fire water spraying nozzle in the workplace in accordance with the technical specifications, from brass material with fire extinguishing, cooling or surface cooling function, spraying on the droplet structure when the water is opened in the open position and at a certain angle. Shall read as new text: SIDE WALL TYPE FIRE SPRINKLER Produced in accordance with the Regulation of 305/2011 / EU Building Materials, made of brass material, with threaded connection, and provided with CE conformity mark and marketed as a result of fire heat, glass or molten metal is turned on and the pressure water behind it is automatically sprayed on fire. Installation of automatic fire sprinklers in accordance with EN 12259-1 in accordance with the drawings, technical and drawing specifications, delivery in working condition. Opening temperature is 57ºC, 68ºC, 79ºC, 93ºC, 100ºC or 141ºC. Item M.133 The former title: STAINLESS GALVANIZED STEEL PIPE Ø15 Shall read as new title: GALVANIZED STEEL PIPE Ø15 Item M.134 The former title: STAINLESS GALVANIZED STEEL PIPE Ø20 Shall read as new title: GALVANIZED STEEL PIPE Ø20 Item M.135 The former title: STAINLESS GALVANIZED STEEL PIPE Ø25 Shall read as new title: GALVANIZED STEEL PIPE Ø25 Item M.136 The former title: STAINLESS GALVANIZED STEEL PIPE Ø32 Shall read as new title: GALVANIZED STEEL PIPE Ø32 Item M.137 The former title: STAINLESS GALVANIZED STEEL PIPE Ø40 Shall read as new title: GALVANIZED STEEL PIPE Ø40 Item M.138 The former title: STAINLESS GALVANIZED STEEL PIPE Ø50 Shall read as new title: GALVANIZED STEEL PIPE Ø50 Item M.139 The former title: STAINLESS GALVANIZED STEEL PIPE Ø65 Shall read as new title: GALVANIZED STEEL PIPE Ø65 Item M.140 The former title: STAINLESS GALVANIZED STEEL PIPE Ø80 Shall read as new title: GALVANIZED STEEL PIPE Ø80 Item M.327 The former title: 2-WAY, PN-10, AUTOMATIC VALVE BODY WITH SCREW Ø 15 MM Shall read as new title: 2-WAY, PN-10, AUTOMATIC VALVE BODY WITH SCREW Ø 15-32 MM Item M.378 Add new text under the heading: Mirrors with fume grey glass in 5mm thickness, with 2 cm bevelling on the edges to be used in WCs in accordance with the designs. Item M.362 The former text: Iron rivets, bolts, welding and all kinds of materials for the construction of stairs, balconies, bridges, balustrades, window and garden stands made of various steel bars, lathes and profiled iron, stairs made to places such as ceiling, septic tank and similar places, and casualty, workplace loading, horizontal and vertical handling, unloading, labour, contractor general expenses and profits. Shall read as new text: Floor drain grate manufactured from 316 quality stainless steel, with a pan inclined and discharged from one side. Pan drainage channels consist of three main parts; top grill, water collection pan and siphon mechanism. Supply and installation of floor drain grate, workplace loading, horizontal and vertical handling, unloading, labour, contractor general expenses and profits. Item E.176 Add new text under the heading: Complementary items such as SFP modules, main switches etc. are included within the scope of the item. Item E.177 Add new text under the heading: Complementary items such as fiber patch cords etc. are included within the scope of the item. Item E.178 The former text: Digital Signal Processing (DSP) 1/3 '' CCD detection sensor. The number of image elements shall be 752 (H) x 582 (V) or better. The scanning system shall be in PAL standard. The scanning system shall be 625 lines, 2: 1 interlace. AC line lock synchronization system. The horizontal resolution shall be 600 TV lines or better. The minimum illumination level shall be 0.1 lux or better at F1.2 30 IRE. The signal-to-noise ratio shall be better than 50dB. AGC (automatic gain control) feature. Backlight compensation, ATW / AWC feature. BNC shall be installed. The supply voltage shall be 24VAC and 12V DC. C / CS Lens shall be available. It should support Auto Iris and DC lenses. Flickerless properties. The operating temperature shall be between -10 ° C and 50 ° C. Shall read as new text: The product must be a fixed IP camera. The camera must have a minimum resolution of 2MP (1920x1080). It must have a 1/2.8 1 CMOS image sensor with progressive scanning technology. It must have 3 - 10.5 mm, with p-iris properties, verifocal, IR-Corrected lens. It must be a camera with a day/night feature. It must have a mechanical IR filter and must be able to do day/night transitions automatically depending on the light condition. It must be able to display colour images up to 0.25 lux and black&white up to 0.05 lux with F1.4 lens. The electronic aperture speed must reach a minimum of 1/33500 per second in order to capture the moving images more clearly. In addition to H.264 Baseline and Main profile formats, it must also be able to display in Motion JPEG format. The camera must be able to move ± 180° horizontally, 90° vertically, and also must have a rotation of 95°. The camera must be able to deliver 25 fps images at 2MP resolution. The display in aspect ratio must be 9:16. With the Multiple stream features, must be capable of broadcasting multiple images with different properties. The number of images and the bandwidth in seconds must be set to a fixed value. Image compression, colour, brightness, sharpness, white balance, backlight light compensation, exposure control, exposure area, low light must be fine-tuned. The camera must have a WDR-Wide dynamic range. The camera must have a special area masking feature. In addition to password protection on the camera, it must have HTTPS encryption, IP address filtering and IEEE 802.1X network access control. The protocols to be supported on the product are: IPv4/v6, HTTP, HTTPs, QoS, FTP, CIFS/SMB, SMTP, Bonjour, UPnP, SNMP v1/v2c/v3 (MIB-II), DNS, DynDNS, NTP, RTSP, RTP , TCP, UDP, IGMP, RTCP, ICMP, DHCP, ARP, SOCKS protocols must be supported. It must have ONVIF support. It must have a video motion detection feature to detect motion. Software updates must be available from the manufacturer's website, and updates must be performed using HTTP or FTP. There must be an image buffer before and after the alarm. In the event of an alarm, the e-mail must be able to provide information via HTTP and TCP and must be able to record an alarm condition to the memory card. It must have remote focus and zoom features to be used during the installation phase. The camera must have IP42 protected IK08 enclosure certificate. The camera must have IEEE 802.3af Class 3 PoE or IEEE 802.3at standard High Power Over Ethernet support. It must have one RJ-45 jack for 10BASE-T/100BASE-TX PoE. There must be a Micro SD/SDHC card slot supporting up to 64 GB. Must support for recording to NAS or File Server. The camera must be able to operate at the ranges of 0°C - 50°C and 10 – 85 % RH relative humidity. Item E.179 The former text: 16 VIDEO INPUT 32 MONITOR OUTPUT MATRIX SWITCHER 100/1000 / 1000Mbps RJ45 Ports (compatible with CAT-5 and similar cables, compatible with IEEE 802.3i, IEEE 802.3u, IEEE 802.3ab and IEEE 802.3x standards, capable of operating at 100-240VAC) Shall read as new text: MONITORING COMPUTER The computer must be in a workstation architecture. The workstation processor must have 64bit architecture. The processor must be at least 3 GHz with at least 4 (four) physical cores. A minimum of 8 GB of memory must be obtained on the workstation using at least 4 GB of DDR4 2133 MHz ECC memory modules. There must be at least 2 x 3.5” appropriate hard disk slots on the workstation. There must be at least 1 x 500 GB-capacity SATA disk on the workstation with a speed of 7,200 rpm. There must be at least 1 x Gigabit Ethernet port on the workstation. There must be at least 350 watt power supply on the workstation. 1 professional workstation VGA card with at least 1 GB GDDR5 memory must be installed on the workstation. There must be 2 HDMI Port outputs on the VGA Card. There must be a DVD-RW unit with 1 SATA-II supported, that can burn on + and - media on the workstation. There must be at least 6 USB ports on the workstation. The workstation motherboard must have a high definition integrated sound card. There must be audio outputs and microphone inputs on the front and back of the case. The workstation must come with a QWERTY keyboard with a Turkish character set and a USB connected mouse. The operating system must be supplied with the workstation to run the IP Camera software. This operating system installation, driver and support CD/DVD and booklets must also be delivered with the workstation. Item E.180 The former text: It shall have 2 internal HDD slots. (240GB HDD capacity) The CD recorder and DAT can be connected to the digital recording device. 5, 25, 50 picture recording speeds in a second. It shall be selected by the user. TCP / IP connection and Ethernet connection. Supply voltage 90V AC-240V AC Continuous recording, recording monitoring, backup, remote access monitoring, remote access recording monitoring shall be done at the same time. Continuous recording, event information and message recording. Inside the area shall be an optional motion detector. PTZ shall be able to control the cameras. Flexible recording options It shall have a support for dynamic IP address. It must have a 32bit RISC processor. There shall be 64MB of RAM. Up to 4TB HDD recording capacity. The compression technique shall be Wavelet. There shall be 16 video inputs. These inputs must carry looping capability. 2 (Main and Spot) BNC and 1 S-Video monitor output. There shall be a display speed of 480 images per second. The recording speed shall be 240 images per second. Wifi, USB, RS232 / RS422 / 485 outputs. 16 alarm inputs and 4 alarm outputs. Supply voltage 90V AC-240V AC The operating temperature shall be between 5 ° C and 45 ° C. Relative humidity shall be 30-80%. All labour costs, material costs, transportation costs, overhead and profit are included in unit price Shall read as new text: The recording server must be 4U high or a tower type. There must be at least 2 processors on the recording server. The recording server shall be delivered with at least 16M Cache, 2.10 GHz xeon based processor. The recording server shall record for 6 months. If a single server is not sufficient, servers shall be added. There shall be at least a 120GB SSD hard disk for the operating system to run on the recording server. The recording server system disk slots must support SAS2 and SATA3 technologies. There must be at least 5 PCI-Express expansion slots on the recording server system board. The main components of the recording server system (motherboard, chassis and power supply) must be the same with the system manufacturer's products. The recording server shall be delivered with at least 2GB of memory on the system and 1 graphics adapter with 128Bit and 2 monitor outputs. The recording server system must have 2 x 1GbE network adapters. There shall be at least 1 x Optical DVD-Writer on the recording server. The recording server system power supply must be highly efficient. The platinum level must be 80Plus certified and must be at least 94% efficient. The recording server system must have power supply redundancy and at least 920W power. The recording server system must be key-lockable from the front. The recording server system must have Windows server 2012 R2 standard or equivalent and the operating system licenses shall be delivered to the administration. Intelligent Video Management software (Software) must be a scalable, enterprise-level product. The software must be able to be installed on commercially available hardware. All functions of the software must be accessible from a single user panel and from the same software manufacturer's software. The software must support the edge failover feature when the server is disabled, record on the sd card on the camera, and take the records on the sd card to the server when the server is enabled. The software must have a flexible licensing model per camera. When an additional camera license is required, a license can be added to the system without obtaining a group camera license or receiving other different license types. Different license types must run on a single server. All licenses must be connected to the server and the camera must not be connected to the MAC address. The software must provide both video management (when needed) and video analysis features from the same manufacturer. The software must have at least the following components. Server software, Windows client software or equivalent, Web client, PDA client The software must be customizable and the Software Development Kit (SDK) will be provided by the manufacturer. All user actions or server errors must be kept in full audit log. The software must be compatible with Microsoft Virtualization technology in VM Ware or Windows Server 2008 or equivalent. The software must support multiple multi-server and multi-location installations from a single server with the following features. The software must be able to operate over a single IP over a gateway through a firewall. There must be dynamic naming support for servers that frequently change IP addresses. It must have one or more server support. Server farm support must be provided if the capacity of a project is over the processing power of a single server. It must have NAS, SAN and local recording support. The software must not have a camera limit per server connected to the license. It must support different viewing and recording options for video broadcasts. MJPEG from the camera at the same time must be able to record MPEG-4 and H.264 video broadcasts. It must be able to record, for each type of stream, in different number of days. Must have capture card support. Integration options: API/SDK Software server Events over TCP/IP; Support for user plug-ins Access control User profiles There must be access per camera. User privileges must be made through user groups and user memberships must be assigned to different groups. It must be able to receive logs and alerts. User actions must be able to be displayed according to time, location and camera. Maps must support the following options: Fixed and active maps that the user can upload (BMP, GIF, JPEG map images) Map icons must be able to show I/O and current status of cameras I/O devices must be enabled on the map. Search options Simple Search (Date and time bound search) Graphical timeline search Flexible time adjustment for pre and post events in search results Make all the qualified video particles into a single movie Saving JPG images of each qualified particle Authentication must support the following features: Microsoft Active Directory user accounts Username + password or equivalent. Item E.185 The former text: OUTSIDE TYPE CAMERA DAY NIGHT Digital Signal Processing (DSP) 1/3 '' CCD detection sensor. The number of image elements shall be 752 (H) x 582 (V) or better. The scanning system shall be in PAL standard. The scanning system shall be 625 lines, 2: 1 interlace. AC line lock synchronization system. The horizontal resolution shall be 600 TV lines or better. The minimum illumination level shall be 0.1 lux or better at F1.2 30 IRE. The signal-to-noise ratio shall be better than 50dB. AGC (automatic gain control) feature. Backlight compensation, ATW / AWC feature. BNC shall be installed. The supply voltage shall be 24VAC and 12V DC. C / CS Lens shall be available. It should support Auto Iris and DC lenses. Flickerless properties. The operating temperature shall be between -10 ° C and 50 ° C Shall read as new text: It must be a box type fixed IP camera. Must have 2 MP (1920x1080) Full HDTV resolution. There must be a 1/2.8 1 CMOS image sensor with progressive scanning technology. There must be a verifocal, IR-Corrected lens with 2.8 to 8 mm, F1.3, P-iris and CS-mount characteristics, providing visibility from 90º to 40º. It must be a camera with a day/night feature. It must have a mechanical IR filter and must be able to do day/night transitions automatically depending on the light condition. It must be able to display a black/white image up to 0.04 lux and colour images up to 0.18 lux with F1.3 lens. The electronic aperture speed must reach a minimum of 1/33500 per second in order to capture the moving images more clearly. In addition to H.264 Baseline and Main profile formats, it must also be able to display in Motion JPEG format. It must display images that can be resized up to 50 fps at resolutions from 1920x1080 to 160x90 The camera must have a feature that enables it to display colour images at low lux values. The camera must have a wide dynamic range and must be able to operate up to 120 db. With the multiple stream features, it must be capable of broadcasting multiple images with different properties. The number of pictures and bandwidth in seconds must be adjustable to a fixed value. Must support multiple view streams with up to 8 individual specified view fields Compression, colour, brightness, sharpness, contrast, white balance, backlight light compensation settings must be adjusted on the image. It must have dynamic contrast feature. It must have a special field masking feature. It must image mirroring feature. The image that comes from the camera in the 16: 9 format must be displayed in 9:16 format. Full duplex audio support must be available. With its integrated microphone, it must be able to carry the sounds in the outdoor environment with the image to the relevant point without the need for an additional device via the IP network. The external microphone and speaker must be able to be connected if necessary. In addition to password protection on the camera, it must have HTTPS encryption, IP address filtering and IEEE 802.1X network access control. Classic IP address configuration IPV4 and next generation IP address configuration IPV6 support must be available. To be managed remotely by 3rd party systems, SNMPV1, V2c, V3 must be supported. If more than one client connects to the camera, the camera must have IGMP (multicast) support to not increase the bandwidth. The camera must have QoS Layer3 DiffServ support for prioritization. It must meet ONVIF standards. It must have a video motion detection feature to detect motion. It must have a tamper alarm feature that shall be activated when the casing of the camera is opened. A pre-built scenario must be triggered by means of an external signal, a high volume or time program. Software updates must be available from the manufacturer's website, and updates must be performed using HTTP and FTP. There must be an image buffer before and after the alarm. In the event of an alarm, the e-mail must be able to provide information via HTTP and TCP and must be able to record an alarm condition to the memory card. To be used during the installation phase, it must have focus assistant, remote back focus and pixel counter. IEEE 802.3af Class 3 PoE must be used for feeding. The camera must also be powered by an 8 - 28 VDC power supply. It must have a RJ45 jack for 10BASE-T/100BASE-TX PoE, and 1 alarm input and relay output. It must have full duplex RS-485 connection with audio input and audio output ports. There must be a Micro SD/SDHC/SDXC card slot supporting up to 64 GB. Support for recording to NAS or File Server. The camera must have IP66, IP67, IK10 and NEMA type 4X approvals. The camera must be able to operate at ranges between -40°C - 50°C temperatures and 10 - 100% RH relative humidity. Item E.212 The former text: Solar Collector case and glass roofs; aluminium material (AlMgSi 0,5), the outer part shall be electrostatic powder painted resistant to weather conditions and corrosion. Case base shall be 0.50 mm Embossed Aluminium. The panel shall consist of blue selective coated copper strips and copper pipes. The frame top cover shall be made of prismatic patterned glass which is resistant to atmospheric events, absorbs the sun rays in the best way and has a thickness of at least 3,2 ± 0,2 mm. Isolation of Solar Collector; the bottom and sides shall be at least 27 mm monolithic polyurethane material on one piece and additionally shall be heat insulated from 20 mm thick aluminium foil coated glass or 50 mm stone wool. Wicks and gaskets to be used in the solar collector shall be resistant to UV rays, impermeable, 100% EPDM rubber material. The solar collector test pressure shall be at least 12 bars and the maximum working pressure 9 bars. At least 70% or more of the daily average thermal efficiencies of planar surface collectors, shall be tested in accordance with EN 12975. With ISO 9001 or equivalent certificate, CE certificate and TSE document. Test reports, certificates and documents shall be presented to the Engineer, and companies with insufficient and incomplete documents shall be excluded from the tender. The proposed solar collector shall be guaranteed for at least two (2) years. The Official Warranty Certificate shall be issued by the manufacturer. Shall read as new text: SOLAR PANELS The total system capacity of the Solar Panel shall be ~ 130 kWp minimum. The PV Solar Panel (Solar Module) power must be 250 Wp and the panels used must be of the same type and power. Solar panels shall be of polycrystalline structure. Snow and wind load shall be Class 3. The solar module frame shall be made of corrosion resistant material and shall be made of stainless steel. Frame must be designed to be installed without any processing such as punching etc. Solar Panel (PV) modules; - shall run smoothly at 40 C to +125 C operating temperatures. This shall be indicated in the technical document presented. Solar Panel (PV) modules; following solar modules with the following information (Standard test conditions 1000 W/m2 radiation 125 C module temperature and AM = 1.5 spectrum conditions) shall be submitted. Voc (Open circuit voltage) Isc (short circuit current) Impp (current at rated power) Vmpp (Voltage at rated power) Pmax values Panel yield (%) Thermal properties (Relation between temperature and module output) Powers of panels, physical dimensions and weight and similar values must be read in the technical document presented. INVERTERS DC voltage produced from solar panels shall be connected to AC power by integrated inverters integrated into the grid. The inverters shall be rated at the power specified in the project and shall be capable of delivering 3 phase 400V AC output in the form of full sine wave at 50 Hz frequency. Maximum input voltage must be 1000 VDC. Maximum yield or “Euro yield” must be at least 97.5%. THD must be < 2 % Inverters must meet at least IP 65 protection standard Operating temperature must cover between -20C to + 60C The following data must be seen on the graphic display on the front of the inverter. Instantaneous power generation Daily energy generation Energy generated as of installation Panel voltage Mains voltage Fault monitoring (DATALOGGING) AND REMOTE MONITORING SYSTEM SES (Solar Energy System) shall be connected to the administration service building with remote access. The SES shall have the ability to record the data from the data logging system by measuring the specified parameters in the overhead. Solar irradiation kWh/m2 Module temperature Ambient temperature For all inverters in SES DC input of the panel array connected to the inverter, current Voltage and instantaneous power Inverter output current, voltage, instantaneous power, frequency and power factor With the remote monitoring system, the total power generated from the panels in the SES during the day, in the last month, in the year, and the amount of CO2 emissions avoided from the installation shall be displayed on the screen numerically and graphically. With the remote monitoring system, error and error messages and warnings of extraordinary events occurring in SES shall be sent to the e-mail addresses and GSM numbers determined by the authorized person immediately. Data recording of the entire team of remote monitoring system, software, hardware, components shall be provided by the contractor. CABLES AND LABOUR Wiring between PV panels, the supply and installation of cables to be used between the solar panels-inverter and the inverter-panel shall be carried out by the contractor. Cables for PV panel connections; There shall be solar cables specially designed for use in PV energy systems The PV power cables shall have the rated cable cross-section, high-temperature and heat-resistant, UV-resistant, double-insulated, halogen-free lead-free (preferably) and shall be manufactured in accordance with the IEC60228, IEC 60287 and IEC60332-1-2 standards approved by the TÜV. The solar cables to be used in the system shall be produced according to the rated voltage of 1800VDC. Solar Cables – must operate smoothly at 40°C/90°C operating temperature. Cables to be laid between the PV panels and the inverters (DC side) shall be in cross-section to allow a maximum voltage drop of 1% at maximum current. The AC (LV) power cables in the 0.6 (zero point)/1 (one) kV series to be drawn between the inverter and the AC bus in the building shall be PVC insulated energy cables suitable for use in the soil suitable for harsh operating conditions. Solar cables must operate at a maximum conductor temperature of 120°C. AC cables shall be manufactured in accordance with TS IEC60502-1 VDE 0276-603 standard with TSE certificate. The maximum working temperature of the AC cables is 70°C. The permitted short circuit temperature shall be 160°C. The cables to be laid between the inverter and the AC common busbar shall be in cross-section to allow a maximum voltage drop of 1% at the maximum power of the SES. MC4 type male and female type connectors shall be used for panel-to-solar and solar cable - inverter connections. Connectors, special couplings and sockets - suitable for high-current, with a protection class of IP 67, suitable for operating temperatures between -400C (minus forty degrees) and 90 0C (ninety degrees). In the panel connection box, a sufficient number of DC surge arresters shall be used in each solar panel group, AC surge arrester at inverter outputs, DC line protection fuse and AC automaton shall be used to disconnect DC +/DC-channel. GROUNDING All electrical and electronic devices belonging to the solar energy system to be installed, all the carrier metal parts, the metal parts and the auxiliary metal mounting materials must be grounded. Grounding in accordance with standards is required. Grounding network shall be made in the area where the panels shall be placed and solar energy system elements and metal components shall be connected to this grounding line. DC Direct current grounding: System grounding (Panel, Inverter, DC box etc.) and protection grounding (Grounding of all metal part without current) CONSTRUCTION The SES to be established shall have a fixed angle configuration structure. The construction that the solar panels shall be installed on must be able to withstand 3800 pascal wind load and minimum 5400 pascal snow load. The construction shall be corrosion resistant (Galvanized iron, aluminium, etc.). The thickness of the galvanized shall be selected such a way that the plant shall operate without corrosion for ten years. The solar panels shall be mounted on the fixing profiles with suitable connection apparatus and the holes on the solar panels shall not be used for the mounting with screws. Panels; Manufactured according to IEC standard 61215 and 61730 DIN, and the test result must be TÜV-Nord certified (No 4478014163101). WARRANTY CONDITIONS Efficiency Guarantee will not be lower than 90 % for 12 years. Aluminium and others must have a 2-year product guarantee. Maintenance of the established system is included for the Defects Notification Period. Related trainings will be arranged by the Contractor to be provided by the manufacturer. INSTALLATION AND REPAIR SERVICES The Contractor shall carry out the assembly process with its own personnel. During the warranty period, maintenance shall be done and shall not charge for this service. REQUIRED SPARE PARTS The contractor shall supply its own spare parts during the installation of the products. In addition, the contractor shall supply the spare parts of the machine itself in the periodic maintenance that it performs every 6 months during the warranty period and shall not charge any money for this service. OTHER PROVISIONS Products shall comply with EN, ISO or CE standards. Making the necessary measurements, Shadow Analysis, Inverter location. Installation field explorations and infrastructure works. Single line diagram and preparation of detail projects. a.) Design of the layout plan. b) All relevant permits and certificated of approvals shall be submitted by the works contractor.

VOLUME 4.3.2 — BILL OF QUANTITIES For all lots: The former title: M.032 OPEN FIRE WATER SPRAY NOZZLE (WHITE PAINTED) Shall read as new title: M.032 SIDE WALL TYPE FIRE SPRINKLER The former title: M.133 STAINLESS GALVANIZED STEEL PIPE Ø15 Shall read as new title: M.133 GALVANIZED STEEL PIPE Ø15 The former title: M.134 STAINLESS GALVANIZED STEEL PIPE Ø20 Shall read as new title: M.134 GALVANIZED STEEL PIPE Ø20 The former title: M.135 STAINLESS GALVANIZED STEEL PIPE Ø25 Shall read as new title: M.135 GALVANIZED STEEL PIPE Ø25 The former title: M.136 STAINLESS GALVANIZED STEEL PIPE Ø32 Shall read as new title: M.136 GALVANIZED STEEL PIPE Ø32 The former title: M.137 STAINLESS GALVANIZED STEEL PIPE Ø40 Shall read as new title: M.137 GALVANIZED STEEL PIPE Ø40 The former title: M.138 STAINLESS GALVANIZED STEEL PIPE Ø50 Shall read as new title: M.138 GALVANIZED STEEL PIPE Ø50 The former title: M.139 STAINLESS GALVANIZED STEEL PIPE Ø65 Shall read as new title: M.139 GALVANIZED STEEL PIPE Ø65 The former title: M.140 STAINLESS GALVANIZED STEEL PIPE Ø80 Shall read as new title: M.140 GALVANIZED STEEL PIPE Ø80 The former title: M.327 2-WAY, PN-10, AUTOMATIC VALVE BODY WITH SCREW Ø 15 MM Shall read as new title: M.327 2-WAY, PN-10, AUTOMATIC VALVE BODY WITH SCREW Ø 15-32 MM The former title: E.179 16 VIDEO INPUT 32 MONITOR OUTPUT MATRIX SWITCHER Shall read as new title: E.179 MONITORING COMPUTER

VOLUME 4.3.3 — PRICE SCHEDULE Add new text: Price No: S.024A Title: DEMOLISHING THE EXISTING CONCRETE/ASPHALT BUILDINGS, ROADS, RUNWAYS AND SIMILAR EXISTING STRUCTURES All kind of materials for construction, workshop expenses, vertical and horizontal transportation in the workplace, unloading, workmanship, contractor’s general expenses and profit is included. This price is per m³ The former text: Price No: M.032 Title: OPEN FIRE WATER SPRAY NOZZLE (WHITE PAINTED) All kind of materials for construction, workshop expenses, vertical and horizontal transportation in the workplace, unloading, workmanship, contractor’s general expenses and profit is included. This price is per pcs Shall read as new text: Price No: M.032 Title: SIDE WALL TYPE FIRE SPRINKLER All kind of materials for construction, workshop expenses, vertical and horizontal transportation in the workplace, unloading, workmanship, contractor’s general expenses and profit is included. This price is per pcs The former text: Price No: M.133 Title: STAINLESS GALVANIZED STEEL PIPE Ø15 All kind of materials for construction, workshop expenses, vertical and horizontal transportation in the workplace, unloading, workmanship, contractor’s general expenses and profit is included. This price is per m Shall read as new text: Price No: M.133 Title: GALVANIZED STEEL PIPE Ø15 All kind of materials for construction, workshop expenses, vertical and horizontal transportation in the workplace, unloading, workmanship, contractor’s general expenses and profit is included. This price is per m The former text: Price No: M.134 Title: STAINLESS GALVANIZED STEEL PIPE Ø20 All kind of materials for construction, workshop expenses, vertical and horizontal transportation in the workplace, unloading, workmanship, contractor’s general expenses and profit is included. This price is per m Shall read as new text: Price No: M.134 Title: GALVANIZED STEEL PIPE Ø20 All kind of materials for construction, workshop expenses, vertical and horizontal transportation in the workplace, unloading, workmanship, contractor’s general expenses and profit is included. This price is per m The former text: Price No: M.135 Title: STAINLESS GALVANIZED STEEL PIPE Ø25 All kind of materials for construction, workshop expenses, vertical and horizontal transportation in the workplace, unloading, workmanship, contractor’s general expenses and profit is included. This price is per m Shall read as new text: Price No: M.135 Title: GALVANIZED STEEL PIPE Ø25 All kind of materials for construction, workshop expenses, vertical and horizontal transportation in the workplace, unloading, workmanship, contractor’s general expenses and profit is included. This price is per m The former text: Price No: M.136 Title: STAINLESS GALVANIZED STEEL PIPE Ø32 All kind of materials for construction, workshop expenses, vertical and horizontal transportation in the workplace, unloading, workmanship, contractor’s general expenses and profit is included. This price is per m Shall read as new text: Price No: M.136 Title: GALVANIZED STEEL PIPE Ø32 All kind of materials for construction, workshop expenses, vertical and horizontal transportation in the workplace, unloading, workmanship, contractor’s general expenses and profit is included. This price is per m The former text: Price No: M.137 Title: STAINLESS GALVANIZED STEEL PIPE Ø40 All kind of materials for construction, workshop expenses, vertical and horizontal transportation in the workplace, unloading, workmanship, contractor’s general expenses and profit is included. This price is per m Shall read as new text: Price No: M.137 Title: GALVANIZED STEEL PIPE Ø40 All kind of materials for construction, workshop expenses, vertical and horizontal transportation in the workplace, unloading, workmanship, contractor’s general expenses and profit is included. This price is per m The former text: Price No: M.138 Title: STAINLESS GALVANIZED STEEL PIPE Ø50 All kind of materials for construction, workshop expenses, vertical and horizontal transportation in the workplace, unloading, workmanship, contractor’s general expenses and profit is included. This price is per m Shall read as new text: Price No: M.138 Title: GALVANIZED STEEL PIPE Ø50 All kind of materials for construction, workshop expenses, vertical and horizontal transportation in the workplace, unloading, workmanship, contractor’s general expenses and profit is included. This price is per m The former text: Price No: M.139 Title: STAINLESS GALVANIZED STEEL PIPE Ø65 All kind of materials for construction, workshop expenses, vertical and horizontal transportation in the workplace, unloading, workmanship, contractor’s general expenses and profit is included. This price is per m Shall read as new text: Price No: M.139 Title: GALVANIZED STEEL PIPE Ø65 All kind of materials for construction, workshop expenses, vertical and horizontal transportation in the workplace, unloading, workmanship, contractor’s general expenses and profit is included. This price is per m The former text: Price No: M.140 Title: STAINLESS GALVANIZED STEEL PIPE Ø80 All kind of materials for construction, workshop expenses, vertical and horizontal transportation in the workplace, unloading, workmanship, contractor’s general expenses and profit is included. This price is per m Shall read as new text: Price No: M.140 Title: GALVANIZED STEEL PIPE Ø80 All kind of materials for construction, workshop expenses, vertical and horizontal transportation in the workplace, unloading, workmanship, contractor’s general expenses and profit is included. This price is per m The former text: Price No: M.327 Title: 2-WAY, PN-10, AUTOMATIC VALVE BODY WITH SCREW Ø 15 MM All kind of materials for construction, workshop expenses, vertical and horizontal transportation in the workplace, unloading, workmanship, contractor’s general expenses and profit is included. This price is per pcs Shall read as new text: Price No: M.327 Title: 2-WAY, PN-10, AUTOMATIC VALVE BODY WITH SCREW Ø 15-32 MM All kind of materials for construction, workshop expenses, vertical and horizontal transportation in the workplace, unloading, workmanship, contractor’s general expenses and profit is included. This price is per pcs The former text: Price No: E.179 Title: 16 VIDEO INPUT 32 MONITOR OUTPUT MATRIX SWITCHER All kind of materials for construction, workshop expenses, vertical and horizontal transportation in the workplace, unloading, workmanship, contractor’s general expenses and profit is included. This price is per pcs Shall read as new text: Price No: E.179 Title: MONITORING COMPUTER All kind of materials for construction, workshop expenses, vertical and horizontal transportation in the workplace, unloading, workmanship, contractor’s general expenses and profit is included. This price is per pcs

All other terms and conditions of the Tender Dossier remain unchanged. The above alterations and / or corrections to the tender dossier are an integral part of the Tender Dossier.

***

CHANGES NO:4 to

TENDER DOSSIER

| Contract Title: | Construction of Removal Centres for the Effective Implementation of the EU – Turkey Readmission Agreement |
| --- | --- |
| Publication Reference: | EuropeAid/139322/IH/WKS/TR |
| Lot 1: | Construction of one Removal Centre in Adana |

The following alterations and/or corrections are made to the Tender Dossier:

VOLUME 4.3.2 — BILL OF QUANTITIES The former text for the lot: VOLUME 4.3.2 BILL OF QUANTITIES Lot - 1: Construction of one Removal Centre in Adana PRICE No TITLE UNIT UNIT PRICE ESTIMATED QUANTITIES AMOUNT (EUR) (a) (b) (c) (d) (e) (f = d * e) MECHANICAL WORKS … M.032 OPEN FIRE WATER SPRAY NOZZLE (WHITE PAINTED) pcs 995,00 … ELECTRICAL WORKS … E.179 16 VIDEO INPUT 32 MONITOR OUTPUT MATRIX SWITCHER pcs 1,00 Shall read as the new text for the lot: VOLUME 4.3.2 BILL OF QUANTITIES Lot - 1: Construction of one Removal Centre in Adana PRICE No TITLE UNIT UNIT PRICE ESTIMATED QUANTITIES AMOUNT (EUR) (a) (b) (c) (d) (e) (f = d * e) MECHANICAL WORKS … M.032 SIDE WALL TYPE FIRE SPRINKLER pcs 139,00 … ELECTRICAL WORKS … E.179 MONITORING COMPUTER pcs 4,00 …

All other terms and conditions of the Tender Dossier remain unchanged. The above alterations and / or corrections to the tender dossier are an integral part of the Tender Dossier.

***

CHANGES NO:4 to

TENDER DOSSIER

| Contract Title: | Construction of Removal Centres for the Effective Implementation of the EU – Turkey Readmission Agreement |
| --- | --- |
| Publication Reference: | EuropeAid/139322/IH/WKS/TR |
| Lot 2: | Construction of one Removal Centre in Kütahya |

The following alterations and/or corrections are made to the Tender Dossier:

VOLUME 4.3.2 — BILL OF QUANTITIES The former text for the lot: VOLUME 4.3.2 BILL OF QUANTITIES Lot - 2: Construction of one Removal Centre in Kütahya PRICE No TITLE UNIT UNIT PRICE ESTIMATED QUANTITIES AMOUNT (EUR) (a) (b) (c) (d) (e) (f = d * e) STRUCTURAL AND ARCHITECTURAL WORKS … S.024 EXCAVATION OF SOFT AND HARD SOIL IN ANY DEPTH AND WIDTH (DEEP EXCAVATION) m³ 34.183,50 … MECHANICAL WORKS … M.032 OPEN FIRE WATER SPRAY NOZZLE (WHITE PAINTED) pcs 1.044,00 … ELECTRICAL WORKS … E.179 16 VIDEO INPUT 32 MONITOR OUTPUT MATRIX SWITCHER Pcs 2,00 … Shall read as the new text for the lot: VOLUME 4.3.2 BILL OF QUANTITIES Lot - 2: Construction of one Removal Centre in Kütahya PRICE No TITLE UNIT UNIT PRICE ESTIMATED QUANTITIES AMOUNT (EUR) (a) (b) (c) (d) (e) (f = d * e) STRUCTURAL AND ARCHITECTURAL WORKS … S.024 EXCAVATION OF SOFT AND HARD SOIL IN ANY DEPTH AND WIDTH (DEEP EXCAVATION) m³ 115.000,00 … MECHANICAL WORKS … M.032 SIDE WALL TYPE FIRE SPRINKLER pcs 160,00 … ELECTRICAL WORKS … E.179 MONITORING COMPUTER pcs 4,00 …

All other terms and conditions of the Tender Dossier remain unchanged. The above alterations and / or corrections to the tender dossier are an integral part of the Tender Dossier.

***

CHANGES NO:4 to

TENDER DOSSIER

| Contract Title: | Construction of Removal Centres for the Effective Implementation of the EU – Turkey Readmission Agreement |
| --- | --- |
| Publication Reference: | EuropeAid/139322/IH/WKS/TR |
| Lot 3: | Construction of one Removal Centre in Malatya |

The following alterations and/or corrections are made to the Tender Dossier:

The following items are added to the Bill of Quantities and scope of works. VOLUME 4.3.2 BILL OF QUANTITIES Lot - 3: Construction of one Removal Centre in Malatya PRICE No TITLE UNIT UNIT PRICE ESTIMATED QUANTITIES AMOUNT (EUR) (a) (b) (c) (d) (e) (f = d * e) ELECTRICAL WORKS ... E.119 4 LOOP, 48 ADDRESS INTELLIGENT ANALOGUE ADRESSABLE FIRE ALARM PANEL pcs 1,00 ...

The following items are removed from the Bill of Quantities and scope of works. VOLUME 4.3.2 BILL OF QUANTITIES Lot - 3: Construction of one Removal Centre in Malatya PRICE No TITLE UNIT UNIT PRICE ESTIMATED QUANTITIES AMOUNT (EUR) (a) (b) (c) (d) (e) (f = d * e) ELECTRICAL WORKS ... E.120 8 LOOP, 48 ADDRESS INTELLIGENT ANALOGUE ADRESSABLE FIRE ALARM PANEL pcs 1,00 ...

The former text for the lot: VOLUME 4.3.2 BILL OF QUANTITIES Lot - 3: Construction of one Removal Centre in Malatya PRICE No TITLE UNIT UNIT PRICE ESTIMATED QUANTITIES AMOUNT (EUR) (a) (b) (c) (d) (e) (f = d * e) MECHANICAL WORKS … M.032 OPEN FIRE WATER SPRAY NOZZLE (WHITE PAINTED) pcs 674,00 … ELECTRICAL WORKS … E.179 16 VIDEO INPUT 32 MONITOR OUTPUT MATRIX SWITCHER pcs 2,00 … Shall read as the new text for the lot: VOLUME 4.3.2 BILL OF QUANTITIES Lot - 3: Construction of one Removal Centre in Malatya PRICE No TITLE UNIT UNIT PRICE ESTIMATED QUANTITIES AMOUNT (EUR) (a) (b) (c) (d) (e) (f = d * e) MECHANICAL WORKS … M.032 SIDE WALL TYPE FIRE SPRINKLER pcs 156,00 … ELECTRICAL WORKS … E.179 MONITORING COMPUTER pcs 4,00

All other terms and conditions of the Tender Dossier remain unchanged. The above alterations and / or corrections to the tender dossier are an integral part of the Tender Dossier.

***

CHANGES NO:4 to

TENDER DOSSIER

| Contract Title: | Construction of Removal Centres for the Effective Implementation of the EU – Turkey Readmission Agreement |
| --- | --- |
| Publication Reference: | EuropeAid/139322/IH/WKS/TR |
| Lot 4: | Construction of one Removal Centre in Niğde |

The following alterations and/or corrections are made to the Tender Dossier:

| VOLUME 4.3.2 — BILL OF QUANTITIES The following items are added to the Bill of Quantities and scope of works. VOLUME 4.3.2 BILL OF QUANTITIES Lot - 4: Construction of one Removal Centre in Niğde PRICE No TITLE UNIT UNIT PRICE ESTIMATED QUANTITIES AMOUNT (EUR) (a) (b) | (c) (d) (e) (f = d * e) ELECTRICAL WORKS ... E.251 6 LOOP, 48 ADDRESS INTELLIGENT ANALOGUE ADRESSABLE FIRE ALARM PANEL pcs 1,00 ... |
| --- | --- |
| The following items are removed from the Bill of Quantities and scope of works. VOLUME 4.3.2 BILL OF QUANTITIES Lot - 4: Construction of one Removal Centre in Niğde PRICE No TITLE UNIT UNIT PRICE ESTIMATED QUANTITIES AMOUNT (EUR) (a) (b) (c) (d) (e) (f = d * e) ELECTRICAL WORKS ... E.119 4 LOOP, 48 ADDRESS INTELLIGENT ANALOGUE ADRESSABLE FIRE ALARM PANEL pcs 1,00 ... |

| The former text for the lot: VOLUME 4.3.2 BILL OF QUANTITIES Lot - 4: Construction of one Removal Centre in Niğde PRICE No TITLE UNIT UNIT PRICE ESTIMATED QUANTITIES AMOUNT (EUR) (a) (b) (c) (d) (e) (f = d * e) STRUCTURAL AND ARCHITECTURAL WORKS … S.285 PROVIDING AND ASSEMBLING OF THE PLAYGROUND EQUIPMENTS FOR KIDS set 1,00 … MECHANICAL WORKS … M.032 OPEN FIRE WATER SPRAY NOZZLE (WHITE PAINTED) pcs 1034,00 … ELECTRICAL WORKS … E.174 700 VA.60 DK.UPS pcs 64,00 … E.179 16 VIDEO INPUT 32 MONITOR OUTPUT MATRIX SWITCHER pcs 5,00 Shall read as the new text for the lot: VOLUME 4.3.2 BILL OF QUANTITIES Lot - 4: Construction of one Removal Centre in Niğde PRICE No TITLE UNIT UNIT PRICE ESTIMATED QUANTITIES AMOUNT (EUR) (a) (b) (c) (d) (e) (f = d * e) STRUCTURAL AND ARCHITECTURAL WORKS … S.285 PROVIDING AND ASSEMBLING OF THE PLAYGROUND EQUIPMENTS FOR KIDS | set 2,00 … MECHANICAL WORKS … M.032 SIDE WALL TYPE FIRE SPRINKLER pcs 158,00 … ELECTRICAL WORKS … E.174 700 VA.60 DK.UPS pcs 2,00 … E.179 MONITORING COMPUTER pcs 2,00 |
| --- | --- |

All other terms and conditions of the Tender Dossier remain unchanged. The above alterations and / or corrections to the tender dossier are an integral part of the Tender Dossier.

***

CHANGES NO:4 to

TENDER DOSSIER

| Contract Title: | Construction of Removal Centres for the Effective Implementation of the EU – Turkey Readmission Agreement |
| --- | --- |
| Publication Reference: | EuropeAid/139322/IH/WKS/TR |
| Lot 5: | Construction of one Removal Centre in Şanlıurfa |

The following alterations and/or corrections are made to the Tender Dossier:

| The following items are added to the Bill of Quantities and scope of works. VOLUME 4.3.2 BILL OF QUANTITIES Lot - 5: Construction of one Removal Centre in Şanlıurfa PRICE No TITLE UNIT UNIT PRICE ESTIMATED QUANTITIES AMOUNT (EUR) (a) (b) (c) (d) (e) (f = d * e) STRUCTURAL AND ARCHITECTURAL WORKS ... S.024A DEMOLISHING THE EXISTING CONCRETE/ASPHALT BUILDINGS, ROADS, RUNWAYS AND SIMILAR EXISTING STRUCTURES m³ 3.132,00 ... ELECTRICAL WORKS ... E.154 FOR 2 FLOOR 1,00 M/SEC. SPEED CLASS 1 HUMAN ELEVATOR MAX WEIGHT: 1275 KG pcs 4,00 ... |
| --- |
| The former text for the lot: VOLUME 4.3.2 BILL OF QUANTITIES Lot - 5: Construction of one Removal Centre in Şanlıurfa PRICE No TITLE UNIT UNIT PRICE ESTIMATED QUANTITIES AMOUNT (EUR) (a) (b) (c) (d) (e) (f = d * e) MECHANICAL WORKS … M.032 OPEN FIRE WATER SPRAY NOZZLE (WHITE PAINTED) pcs 2.856,00 | … ELECTRICAL WORKS ... E.153 FOR 3 FLOOR 1,00 M/SEC. SPEED CLASS 1 HUMAN ELEVATOR MAX WEIGHT: 1275 KG pcs 4,00 E.155 FOR 3 FLOOR 1,00 M/SEC. SPEED CLASS 1 HUMAN ELEVATOR MAX WEIGHT: 1000 KG pcs 2,00 ... E.179 16 VIDEO INPUT 32 MONITOR OUTPUT MATRIX SWITCHER pcs 1,00 … Shall read as the new text for the lot: VOLUME 4.3.2 BILL OF QUANTITIES Lot - 5: Construction of one Removal Centre in Şanlıurfa PRICE No TITLE UNIT UNIT PRICE ESTIMATED QUANTITIES AMOUNT (EUR) (a) (b) (c) (d) (e) (f = d * e) MECHANICAL WORKS … M.032 SIDE WALL TYPE FIRE SPRINKLER pcs 179,00 … ELECTRICAL WORKS ... E.153 FOR 3 FLOOR 1,00 M/SEC. SPEED CLASS 1 HUMAN ELEVATOR MAX WEIGHT: 1275 KG pcs 2,00 E.155 FOR 3 FLOOR 1,00 M/SEC. SPEED CLASS 1 HUMAN ELEVATOR MAX WEIGHT: 1000 KG pcs 1,00 … E.179 MONITORING COMPUTER pcs 4,00 … |
| VOLUME 5 DESIGN DOCUMENTS, INCLUDING DRAWINGS Following design documents are revised via publication: Appendix 2 - 1051-URF-RAB-000 Appendix 3 - 1051-URF-PFA-151 |

All other terms and conditions of the Tender Dossier remain unchanged. The above alterations and / or corrections to the tender dossier are an integral part of the Tender Dossier.

***

CHANGES NO:4 to

TENDER DOSSIER

| Contract Title: | Construction of Removal Centres for the Effective Implementation of the EU – Turkey Readmission Agreement |
| --- | --- |
| Publication Reference: | EuropeAid/139322/IH/WKS/TR |
| Lot 6: | Construction of one Removal Centre in Balıkesir |

The following alterations and/or corrections are made to the Tender Dossier:

The following items are added to the Bill of Quantities and scope of works. VOLUME 4.3.2 BILL OF QUANTITIES Lot - 6: Construction of one Removal Centre in Balıkesir PRICE No TITLE UNIT UNIT PRICE ESTIMATED QUANTITIES AMOUNT (EUR) (a) (b) (c) (d) (e) (f = d * e) STRUCTURAL AND ARCHITECTURAL WORKS … S.024A DEMOLISHING THE EXISTING CONCRETE/ASPHALT BUILDINGS, ROADS, RUNWAYS AND SIMILAR EXISTING STRUCTURES m³ 50,00 ... S.075C CURTAIN WALL (WITH GLAZING WORKS WITH 6+6MM THICK AND 16MM AIR VOID TEMPERED CREATIVE SOLAR CONTROL GLASS) WITH SEMI LIDDED ALUMINIUM PROFILES m² 466,85 ... ELECTRICAL WORKS ... E.251 6 LOOP, 48 ADDRESS INTELLIGENT ANALOGUE ADRESSABLE FIRE ALARM PANEL pcs 1,00 ...

The following items are removed from the Bill of Quantities and scope of works. VOLUME 4.3.2 BILL OF QUANTITIES Lot - 6: Construction of one Removal Centre in Balıkesir PRICE No TITLE UNIT UNIT PRICE ESTIMATED QUANTITIES AMOUNT (EUR) (a) (b) (c) (d) (e) (f = d * e) ELECTRICAL WORKS ... E.120 8 LOOP, 48 ADDRESS INTELLIGENT ANALOGUE ADRESSABLE FIRE ALARM PANEL pcs 1,00 ...

The former text for the lot: VOLUME 4.3.2 BILL OF QUANTITIES Lot - 6: Construction of one Removal Centre in Balıkesir PRICE No TITLE UNIT UNIT PRICE ESTIMATED QUANTITIES AMOUNT (EUR) (a) (b) (c) (d) (e) (f = d * e) STRUCTURAL AND ARCHITECTURAL WORKS … S.066 ALUMINUM STABLE SUNSHADE m² 466,85 … MECHANICAL WORKS … M.032 OPEN FIRE WATER SPRAY NOZZLE (WHITE PAINTED) pcs 1.261,00 … ELECTRICAL WORKS ... E.179 16 VIDEO INPUT 32 MONITOR OUTPUT MATRIX SWITCHER pcs 1,00 … Shall read as the new text for the lot: VOLUME 4.3.2 BILL OF QUANTITIES Lot - 6: Construction of one Removal Centre in Balıkesir PRICE No TITLE UNIT UNIT PRICE ESTIMATED QUANTITIES AMOUNT (EUR) (a) (b) (c) (d) (e) (f = d * e) STRUCTURAL AND ARCHITECTURAL WORKS … S.066 ALUMINUM STABLE SUNSHADE m² 34,30 … MECHANICAL WORKS … M.032 SIDE WALL TYPE FIRE SPRINKLER pcs 96,00 … ELECTRICAL WORKS … E.179 MONITORING COMPUTER pcs 4,00 …

All other terms and conditions of the Tender Dossier remain unchanged. The above alterations and / or corrections to the tender dossier are an integral part of the Tender Dossier.

***