# TENDER: EuropeAid/120072/D/S/TR

Supply of IT Equipment and Software to Support the Turkish Public Internal Financial Control System

CORRIGENDUM No. 2

The following alterations and/ or corrections are made to the Tender Dossier:

Page 87: (Technical Specifications, Article 9)

The former text:

| Software | Backup automation software must be proposed with appropriate licensing for tape drives, media slots and proposed servers. Must be an automated software for all NAS backup needs. |
| --- | --- |

Shall read as new text:

| Software | Backup automation software must be proposed with appropriate licensing for tape drives, media slots and proposed servers. Must be an automated software for all SAN backup needs. |
| --- | --- |

Page 78: (Technical Specifications, Article 1)

The former text:

| General characteristics | Must be hardware or software based. If a software based firewall is proposed it must be compatible with UNIX / Linux and/or Windows based OS’s. |
| --- | --- |

Shall read as new text:

| General characteristics | Must be hardware or software based. If a software based firewall is proposed it must be compatible with UNIX / Linux based OS’s. |
| --- | --- |

Page 79: (Technical Specifications, Article 2)

The former text:

| Other characteristics | Must be hardware or software based. If a software based firewall is proposed it must be compatible with UNIX / Linux and/or Windows based OS’s.. |
| --- | --- |

Shall read as new text:

| Other characteristics | Must be hardware or software based. If a software based firewall is proposed it must be compatible with UNIX / Linux based OS’s. |
| --- | --- |

Page 80: (Technical Specifications, Article 3)

The former text:

| Other characteristics | Must be hardware or software based. If a software based firewall is proposed it must be compatible with UNIX / Linux and/or Windows based OS’s.. |
| --- | --- |

Shall read as new text:

| Other characteristics | Must be hardware or software based. If a software based firewall is proposed it must be compatible with UNIX / Linux based OS’s. |
| --- | --- |

Page 81: (Technical Specifications, Article 4)

The former text:

| Supported Protocols | The switch must support at least IEEE802.3, 802.3u (Fast Ethernet), 802.3z (Gigabit Ethernet), 802.3ab (1000BaseT) and 802.5 (Token Ring / FDDI) standards. |
| --- | --- |
| OS Update | The switch must support at least TFTP for firmware and Operating System upgrades. |

Shall read as new text:

| Supported Protocols | The switch must support at least IEEE802.3, 802.3u (Fast Ethernet), 802.3z (Gigabit Ethernet), 802.3ab (1000BaseT). |
| --- | --- |
| OS Update | The switch must support at least TFTP or FTP for firmware and Operating System upgrades. |

Page 83: (Technical Specifications, Article 5)

The former text:

| Supported Protocols | The backbone switch must support at least IEEE802.3, 802.3u (Fast Ethernet), 802.3z (Gigabit Ethernet), 802.3ab (1000BaseT), 802.3ae (10 Gbit Ethernet) and 802.5 (Token Ring / FDDI) standards. |
| --- | --- |

Shall read as new text:

| Supported Protocols | The backbone switch must support at least IEEE802.3, 802.3u (Fast Ethernet), 802.3z (Gigabit Ethernet), 802.3ab (1000BaseT), 802.3ae (10 Gbit Ethernet). |
| --- | --- |

Page 84: (Technical Specifications, Article 6)

The former text:

| Intrusion Detection System | Proposed IDS can be hardware / appliance based or Software based. |
| --- | --- |

Shall read as new text:

| Intrusion Detection System | Proposed IDS can be hardware / appliance based. |
| --- | --- |

Page 87: (Technical Specifications, Article 9)

The former text:

| Other characteristics | The connection between the DBMS system and the Tape Library must be done over NAS ports described for the Storage Array. |
| --- | --- |

Shall read as new text:

| Other characteristics | The connection between the DBMS system and the Tape Library must be done over SAN ports described for the Storage Array. |
| --- | --- |

Page 88: (Technical Specifications, Servers, General Requirements)

The former text:

All the necessary hardware and software components to connect the servers to the NAS must be proposed.

Shall read as new text:

All the necessary hardware and software components to connect the servers to the SAN must be proposed.

Page 90: (Technical Specifications, Article 11)

The former text:

| Processor | Two 64-bit CPUs. Must be upgradeable to 4 CPU’s over the system without any additional hardware or application of clustering. |
| --- | --- |

Shall read as new text:

| Processor | Two 64-bit CPUs with a minimum 2.2 GHz clock speed. Must be upgradeable to 4 CPU’s over the system without any additional hardware or application of clustering. |
| --- | --- |

Page 95: (Technical Specifications, Article 17)

The former text:

| Screen Type | TFT screen with wide viewing angle |
| --- | --- |
| Screen Size (diagonal) | 19” |

Shall read as new text:

| Screen Type | CRT screen |
| --- | --- |
| Screen Size (diagonal) | 17” |

Page 102: (Technical Specifications, Article 24)

The former text:

| Supported Protocols | The switch must support at least IEEE802.3, 802.3u (Fast Ethernet), 802.3z (Gigabit Ethernet), 802.3ab (1000BaseT) and 802.5 (Token Ring / FDDI) standards. |
| --- | --- |
| IPv6 | The switch must support IPv6 packet routing. |
| OS Update | The switch must support at least TFTP for firmware and Operating System upgrades. |
| Access Management | The switch must be able to classify packets on L2, L3 and L4 protocols. It must support port and time based access lists. |
| DHCP | The switch must support DHCP Server and DHCP Relay functionality. |

Shall read as new text:

| Supported Protocols | The switch must support at least IEEE802.3, 802.3u (Fast Ethernet), 802.3z (Gigabit Ethernet), 802.3ab (1000BaseT). |
| --- | --- |
| IPv6 | The switch must support IPv6 packet switching. |
| OS Update | The switch must support at least TFTP of FTP for firmware and Operating System upgrades. |
| Access Management | The switch must support port and time based access lists. |

Page 104: (Technical Specifications, Article 25)

The former text:

| Processor | Two 64-bit CPUs. Must be upgradeable to 4 CPU’s over the system without any additional hardware. |
| --- | --- |
| Form Factor | Desktop or Tower |

Shall read as new text:

| Processor | Two 64-bit CPUs with a minimum 2.2 GHz clock speed. Must be upgradeable to 4 CPU’s over the system without any additional hardware. |
| --- | --- |
| Form Factor | Desktop, Tower or Rack Mount |

Pages 115, 116: (Technical Specifications, Article 33, 34)

The former text:

| Specific requirements | Provision must be made to allow the server software to operate on a different, but equivalent server in the event of hardware failover. |
| --- | --- |

Shall read as new text:

| Specific requirements | Provision must be made to allow the server software to operate on a different, but equivalent server in the event of hardware failure. |
| --- | --- |

Page 116: (Technical Specifications, Article 35)

The former text:

| General Characteristics | The software must be a web application. The software must be Java Application Server based Servlet type for easy expansion. The software must have an API for easy interfacing. The software must be ISO 17799 and BS 7799 based Information Security tool. |
| --- | --- |

Shall read as new text:

| General Characteristics | The software must be a web application. The software must be Java Application Server based Servlet type for easy expansion. The software must have an API for easy interfacing. The software must have “workflow capability”. The software must be ISO 17799 and BS 7799 based Information Security tool. |
| --- | --- |

Page 147: (Technical Specifications, Article 51)

The former text:

| Phase 1 | Contractor must present detailed CV’s, including work experiences and their roles in the project as a detailed appendix to his proposal. |
| --- | --- |

Shall read as new text:

| Phase 1 | ALL expert CV's can be provided at the time of contracting provided that all required declarations regarding qualifications and nationality of experts are given at the time of proposal. |
| --- | --- |

Page 149: (Technical Specifications, Article 51, Project Team Requirements)

The former text:

Project Team Requirements

Minimum project team requirements are given below. A draft project and team schedule for the experts will be presented to the beneficiary following the signing of the contract.  After the beneficiary approves the list and the schedule the team will start the project. The draft schedule must clearly specify the number of actual experts, their duration of work and the periods in which the experts will be working.

| Job Title/Role | Mains Responsibilities/Functions | Total Years of Experience | Years of Experience in Similar Turnkey Project |
| --- | --- | --- | --- |
| Project Manager | Assumes overall responsibility for the implementation of this project. Will also be responsible for ensuring that the Tenderer’s team delivers the specification of the requirements for hardware and networking services necessary to facilitate the overall solution. Will thereafter liaise with client managers, and any sub-contractors, to timely provide the system requirements. | 15 | 5 |
| Risk Assessor | Defines risks for the execution of the project, development of system and software; and plans mitigation. Plans for the risk management steps Tracks risks, takes timely corrective actions and reports them. | 10 | 2 |
| QA Manager | Is responsible for the execution of the project as per quality requirements set forth in this Technical Specifications Document. Plans for steps for quality, follows them, and makes the results visible to the Client. | 10 | 2 |
| Change Manager | Defines and tracks the changes required in the system and software and reports them to the approval of the Consultant. Coordinates with the Problem Resolution Manager. | 10 | 2 |
| Problem Resolution Manager | Responsible for problems and incidents associated with the successful execution of the development, deployment and operations. Coordinates with Help Desk/Call Center. | 10 | 2 |
| Training Manager | Determines training requirements, plans for, and manages delivery of training modules to the designated audience. Reports results. Coordinates with the vendors. | 10 | 2 |
| Chief Architect | Knowledge and experience in system architecture, standards, system and software design, at least five years of hands on experience in hardware and software components. Knowledge in performance management. Knowledge in performance management. He/she must be experienced on fields related to public financial management and financial audit. |  |  |
| Process Management Expert | Design the processes for the overall execution of the system. The expert must have at least 5 years of experience in process design and management. Experience in inspection and audit processes is essential. He/she must be experienced on fields related to financial audit, and case management. | 15 | 5 |
| Workflow Management Expert | Designs and develops workflows and forms. Must be experienced in the proposed WFM components. | 5 | 3 |
| Configuration Manager | Defines tracks and controls all configuration items in the system solution. | 5 | 2 |
| Senior System Engineer | Responsible for the system design and implementation of overall system. Coordinates with all Experts. | 5 | 2 |
| Senior Network Engineer | Responsible for the network design and IP planning. Coordinates with the system engineer. Network engineer is responsible for daily monitoring and management of the overall system solution through the control console at the central site. | 5 | 2 |
| Senior Security Engineer | Responsible for design of overall security of the system as per ISO 17799. Performs also the internal security audits. Must have at least five years of hands on experience in security system design and implementation of relevant hardware and software. He/she must hold an international certificate such as CISSP, CISA and must have at least five years of experience in designing and implementing security systems including hardware and software. | 10 | 5 |
| Senior Software Engineers | Responsible for the software analysis, design and implementation of application software. At least one of the senior engineers must be experienced on fields related to public financial management, financial audit, and case management. At least one of the senior engineers must be experienced Excel add-ins. | 10 | 5 |
| Help Desk Support Expert | Managing, configuration, development and support of Help Desk Solution(1man/year) | 5 | 2 |
| Test Engineer | Designs test cases, manages tests and documents results. | 5 | 2 |
| Risk Management Expert | Experience in risk management and the relevant tool are essential. | 5 | 2 |
| CAAT Expert | Experience in inspection/audit processes and the relevant tool are essential. | 5 | 2 |

Shall read as new text:

Project Team Requirements

Minimum project team requirements are given below. A draft project and team schedule for the experts will be presented to the beneficiary following the signing of the contract.  After the beneficiary approves the list and the schedule the team will start the project. The draft schedule must clearly specify the number of actual experts, their duration of work and the periods in which the experts will be working.

| Job Title/Role | Mains Responsibilities/Functions | Total Years of Experience | Years of Experience in Similar Turnkey Project | Minimum Work (man/days) |
| --- | --- | --- | --- | --- |
| Project Manager | Assumes overall responsibility for the implementation of this project. Will also be responsible for ensuring that the Tenderer’s team delivers the specification of the requirements for hardware and networking services necessary to facilitate the overall solution. Will thereafter liaise with client managers, and any sub-contractors, to timely provide the system requirements. | 15 | 5 | 180 |
| Risk Assessor | Defines risks for the execution of the project, development of system and software; and plans mitigation. Plans for the risk management steps Tracks risks, takes timely corrective actions and reports them. | 10 | 2 | 30 |
| QA Manager | Is responsible for the execution of the project as per quality requirements set forth in this Technical Specifications Document. Plans for steps for quality, follows them, and makes the results visible to the Client. | 10 | 2 | 30 |
| Change Manager | Defines and tracks the changes required in the system and software and reports them to the approval of the Consultant. Coordinates with the Problem Resolution Manager. | 10 | 2 | 30 |
| Problem Resolution Manager | Responsible for problems and incidents associated with the successful execution of the development, deployment and operations. Coordinates with Help Desk/Call Center. | 10 | 2 | 30 |
| Training Manager | Determines training requirements, plans for, and manages delivery of training modules to the designated audience. Reports results. Coordinates with the vendors. | 10 | 2 | 30 |
| Chief Architect | Knowledge and experience in system architecture, standards, system and software design, at least five years of hands on experience in hardware and software components. Knowledge in performance management. Knowledge in performance management. He/she must be experienced on fields related to public financial management and financial audit. | 10 | 2 | 30 |
| Process Management Expert | Design the processes for the overall execution of the system. The expert must have at least 5 years of experience in process design and management. Experience in inspection and audit processes is essential. He/she must be experienced on fields related to financial audit, and case management. | 15 | 5 | 30 |
| Workflow Management Expert | Designs and develops workflows and forms. Must be experienced in the proposed WFM components. | 5 | 3 | 30 |
| Configuration Manager | Defines tracks and controls all configuration items in the system solution. | 5 | 2 | 30 |
| Senior System Engineer | Responsible for the system design and implementation of overall system. Coordinates with all Experts. | 5 | 2 | 30 |
| Senior Network Engineer | Responsible for the network design and IP planning. Coordinates with the system engineer. Network engineer is responsible for daily monitoring and management of the overall system solution through the control console at the central site. | 5 | 2 | 30 |
| Senior Security Engineer | Responsible for design of overall security of the system as per ISO 17799. Performs also the internal security audits. Must have at least five years of hands on experience in security system design and implementation of relevant hardware and software. He/she must hold an international certificate such as CISSP, CISA and must have at least five years of experience in designing and implementing security systems including hardware and software. | 10 | 5 | 30 |
| Senior Software Engineers | Responsible for the software analysis, design and implementation of application software. At least one of the senior engineers must be experienced on fields related to public financial management, financial audit, and case management. At least one of the senior engineers must be experienced Excel add-ins. | 10 | 5 | 30 |
| Help Desk Support Expert | Managing, configuration, development and support of Help Desk Solution(1man/year) | 5 | 2 | 30 |
| Test Engineer | Designs test cases, manages tests and documents results. | 5 | 2 | 30 |
| Risk Management Expert | Experience in risk management and the relevant tool are essential. | 5 | 2 | 30 |
| CAAT Expert | Experience in inspection/audit processes and the relevant tool are essential. | 5 | 2 | 30 |

All other terms and conditions of the Tender dossier remain unchanged. The above alterations and / or corrections to the tender dossier are an integral part of the Tender Dossier.