CHANGES NO: 1 TO TENDER DOSSIER

Contract Title	: Supply of Equipment for Implementation of Stock Assessments in Fisheries Activities - Relaunch

Publication Reference	: 	EuropeAid/139233/IH/SUP/TR

CN: Contract Notice

TD: Tender Dossier

DOC: Document

ART: Article

ITT: c4b_itt_en [Instructions to Tenderers]*

DC : c4c_contract_en [Draft Contract]*

TS: c4f_annexiitechspeciiitechoffer_en [Annex II + III: Technical Specifications + Technical Offer]*

SC: c4d_specialconditions_en [Special Conditions]*

BB: Annex IV: Budget breakdown (Model financial offer)

* In-parenthesis parts show the title inside the documents.

| Line | DOC | ART / ITEM | FORMER TEXT | SHALL READ AS NEW TEXT |
| --- | --- | --- | --- | --- |
| 1 | ITT | 1.1 / 1.1.7 | Hydrophone: 10 | Hydrophone: 9 |
| 2 | DC | / 1.1.7 | Hydrophone: 10 | Hydrophone: 9 |
| 3 | BB | 1.1.7 | Hydrophone: 10 | Hydrophone: 9 |
| 4 | TS | 1.1.1.2 | An elevator system will be located over the Buoy to enable the up-down movement of the probes for the measurements in different sea depths. (…) | An automated elevator system will be located over the Buoy to enable the up-down movement of the probes for the measurements in different sea depths. (…) |
| 5 | TS | 1.1.3.2 | Lifetime: Min. 12 years | Design Life: Min. 12 years |
| 6 | TS | 1.1.8.7 | Data transfer with ethernet and wifi. | Data transfer with ethernet and/or wifi. |
| 7 | TS | 1.1.15.11 | Languages: English, Turkish. | Languages: English and/or Turkish. |
| 8 | TS | 1.2.9 | Operation Mode: Remote control. | [DELETED] |
| 9 | TS | 1.2.11 | [ADDED AS A NEW SPECIFICATION] | The AUV will be delivered with its transport case. |
| 10 | TS | 2.1.2 | The central equipment shall be the termination point of SSL tunnels established from each end point equipment. | The central equipment shall be the termination point of SSL / VPN tunnels established from each end point equipment |
| 11 | TS | 2.3.6 | Ports: Minimum 1 serial, 8 USB ports (internal and/or external), microphone, headphone, 1 RJ45 Network connector. | Ports: Minimum 1 serial (with or without header), 8 USB ports (internal and/or external), microphone, headphone, 1 RJ45 Network connector |
| 12 | TS | 2.3.11 | Form factor: of the workstation should be mini tower. | Form factor: of the workstation should be tower or mini tower. |
| 13 | Appendix A to Annex II+III Installation / Delivery Locations and Sea Conditions |  | [ADDED AS A NEW SPECIFICATION] | Sea depth will be between 40 – 60 metres for all coordinates where the buoys will be deployed. |
| 14 | Appendix E to Annex II + III Training Proposal Form |  | [ADDED AS A NEW SPECIFICATION] | Lot Number Description Training Requirement 1 Security, reliability, accuracy, installation and ease of maintenance of the AUV along with the units which shall be mounted on it. Number of participant: At least 9 staff of the Beneficiary (6 of them will be out of the hosting city) shall participate. Travel and half-board accommodation costs of the participants attending from out of the hosting city shall be covered by the Contractor. Duration: Minimum 2 days. Place: The trainings shall be delivered in Trabzon on the ship of the Beneficiary which shall be located to the near of the AUV. During the trainings, lunch and coffee breaks (at least 2) shall be given for the participants and the incurred costs shall be covered by the Contractor. |

All other terms and conditions of the tender dossier remain unchanged. The above alterations and /or corrections to the tender dossier are integral part of the tender dossier.

***